TOSHIBA PCI to PC-Card16/CardBus Controller ToPIC100

Specification (2): Register

Draft( Rev. 01.4 ) 1998-10-07

# Contents

6	 Internal Registe…………………………………………………………………………………………………………………….5

6.1	Register ………………………………………………………………………………..……… ……………..……….………………………..5

6.1.1PC-Card Configuration MAP	..5

6.1.2PC-Card 16 Register	6

6.1.3PC-Card 16 Register - continued	7

6.1.4CardBus Register	7

7	 ToPIC100 Configuration Register	8

7.1	Vendor ID Register	8

7.2	Device ID Register	8

7.3	Command Register	9

7.4	Status Register	11

7.5	Revision ID Register	13

7.6	Class Code Register	13

7.7	Header Type Register	13

7.8	Base Address Register	13

7.9	Capability Pointer Register	15

7.10	Secondary Status Register	15

7.11	PCI Bus Number Register	17

7.12	Secondary Bus Number Register	17

7.13	Subordinate Bus Number Register	17

7.14	1st Memory window Base Register	18

7.15	1st Memory window Limit Register	18

7.16	2nd Memory window Base Register	19

7.17	2nd Memory window Limit Register	19

7.18	1st I/O window Base(Lower) Register	20

7.19	1st I/O window Base(Upper) Register	20

7.20	1st I/O window Limit(Lower) Register	20

7.21	1st I/O window Limit(Upper) Register	20

7.22	2nd I/O window Base(Lower) Register	21

7.23	2nd I/O window Base(Upper) Register	21

7.24	2nd I/O window Limit(Lower) Register	21

7.25	2ndI/O window Limit(Upper) Register	21

7.26	Interrupt Line Register	22

7.27	Interrupt Pin Register	22

7.28	Bridge Control Register	23

7.29	Subsystem Vendor ID Register	26

7.30	Subsystem Device ID Register	26

7.31	PC Card16 Legacy Mode Base Address Register	26

7.32	Capability ID Register	27

7.33	Next Item Ptr Register	27

7.34	Power Management Capabilities (PMC) Register	28

7.35	Power Management Control/Status (PMCSR) Register	29

7.36	PMCSR PCI to CardBus Bridge Support Extensions Register	30

7.37	Data Register	30

7.38	CardBus Socket Power Detect Control Register	31

7.39	ZV Control Register	32

7.40	Slot Control Register	33

7.41	Interrupt Control Register	34

7.42	Card Detect Control Register	35

7.43	CardBus Socket Register Control Register	36

7.44	Wake Up Control Register	38

7.45	Serial Interrupt Control Register	40

7.46	MISC1 Register	41

7.47	ZV Configuration Register	42

7.48	BUFFER CONTROL Register	43

7.49	Debug Register	44

7.50	Serial Power Control Register	46

7.51	IRQ Routing Register	47

7.52	Additional Control Register	49

7.53	Configuration Control Register	50

8	 PC-Card16 Register	53

8.1	Identification and Revision Register	53

8.2	Interface Status Register	54

8.3	Power Control Register	55

8.4	Interrupt and General Control Register	58

8.5	Card Status Change Register	59

8.6	Card Status Change Interrupt Control Register	61

8.7	Window Enable Register	63

8.8	I/O Window Control Register	65

8.9	I/O Window 0 Start Low Address Register	67

8.10	I/O Window 0 Start High Address Register	67

8.11	I/O Window 0 Stop Low Address Register	67

8.12	I/O Window 0 Stop High Address Register	67

8.13	I/O Window 1 Start Low Address Register	68

8.14	I/O Window 1 Start High Address Register	68

8.15	I/O Window 1 Stop Low Address Register	68

8.16	I/O Window 1 Stop High Address Register	68

8.17	Memory Window 0 Start Low Address Register	69

8.18	Memory Window 0 Start High Address Register	69

8.19	Memory Window 0 Stop Low Address Register	70

8.20	Memory Window 0 Stop High Address Register	70

8.21	Memory Window 0 Offset Low Address Register	71

8.22	Memory Window 0 Offset High Address Register	71

8.23	Additional General Control Register	72

8.24	Memory Window 1 Start Low Address Register	74

8.25	Memory Window 1 Start High Address Register	74

8.26	Memory Window 1 Stop Low Address Register	75

8.27	Memory Window 1 Stop High Address Register	75

8.28	Memory Window 1 Offset Low Address Register	76

8.29	Memory Window 1 Offset High Address Register	76

8.30	Global Control Register	77

8.31	Memory Window 2 Start Low Address Register	78

8.32	Memory Window 2 Start High Address Register	78

8.33	Memory Window 2 Stop Low Address Register	79

8.34	Memory Window 2 Stop High Address Register	79

8.35	Memory Window 2 Offset Low Address Register	80

8.36	Memory Window 2 Offset High Address Register	80

8.37	Memory Window 3 Start Low Address Register	81

8.38	Memory Window 3 Start High Address Register	81

8.39	Memory Window 3 Stop Low Address Register	82

8.40	Memory Window 3 Stop High Address Register	82

8.41	Memory Window 3 Offset Low Address Register	83

8.42	Memory Window 3 Offset High Address Register	83

8.43	Memory Window 4 Start Low Address Register	84

8.44	Memory Window 4 Start High Address Register	84

8.45	Memory Window 4 Stop Low Address Register	85

8.46	Memory Window 4 Stop High Address Register	85

8.47	Memory Window 4 Offset Low Address Register	86

8.48	Memory Window 4 Offset High Address Register	86

8.49	ToPIC100 Card Timing Register	87

8.50	Audio/Video Switching Register	88

8.51	ToPIC100 Function Control Register	89

9	CardBus Register	90

9.1	Socket Event Register	90

9.2	Socket Mask Register	91

9.3	Socket Present State Register	92

9.4	Socket Force Register	95

9.5	Power Control Register	98

# Internal Register

## Register

### PC-Card Configuration MAP

| 31 | 23 | 15 | 07 | 00 | Port |
| --- | --- | --- | --- | --- | --- |
| Device ID(0617h) | Vendor ID(1179h) | 00h |
| Status(0490h) | Command(0000h) | 04h |
| Class Code(060700h) | Revision ID(00h) | 08h |
|  | Header Type(82h) |  |  | 0Ch |
| Base Address | 10h |
| Secondary Status | Latency Timer | Capability Pointer | 14h |
|  | Subordinate Bus Number | Secondary Bus Number | PCI Bus Number | 18h |
| 1st Memory window Base | 1Ch |
| 1st Memory window Limit | 20h |
| 2nd Memory window Base | 24h |
| 2nd Memory window Limit | 28h |
| 1st I/O window Base (Upper) | 1st I/O window Base (Lower) | 2Ch |
| 1st I/O window Limit (Upper) | 1st I/O window Limit (Lower) | 30h |
| 2nd I/O window Base (Upper) | 2nd I/O window Base (Lower) | 34h |
| 2nd I/O window Limit (Upper) | 2nd I/O window Limit (Lower) | 38h |
| Bridge Control | Interrupt Pin | Interrupt Line | 3Ch |
| Subsystem Device ID(0000h) | Subsystem Vendor ID(0000h) | 40h |
| PC Card16 Legacy Mode Base Address | 44h |
|  |  |  |  | 48h-7Fh |
| Power Management Capabilities (PMC) | Next Item Ptr | Capability ID | 80h |
| Data | PMCSR PCI to CardBus Bridge Support | Power Management Control/Status (PMCSR) | 84h |
|  |  |  |  | 88h |
| TOSHIBA RESERVED | 8Ch 90h |
| CardBus Socket Power Detect Control |  |
|  |  |  |  | 94h-9Bh |
|  |  |  | ZV Control | 9Ch |
| Card Detect Control |  | Interrupt Control | Slot Control | A0h |
| CardBus Socket Register Control | A4h |
| Wake Up Control | A8h |
| Internal PCI Retry | ZV Configuration | MISC1 | Serial Interrupt Control | ACh |
| TOSHIBA RESERVED |  |  |  | B0h |
| TOSHIBA RESERVED |  |  |  | B4h |
| Debug | TOSHIBA RESERVED |  |  | B8h |
|  | Serial Power Control | TOSHIBA RESERVED | BCh |
| IRQ Routing | C0h |
|  |  |  | Additional Control | C4h |
|  |  |  |  | C8-FBh |
| Configuration Control | FCh |

### 6.1.2    PC-Card 16 Register

(1)Base Address :Slot Control Register (A0h/Device ID:0617h)

(2)Base Address :Base Address(10h/Device ID:0617h)

| Offset(1) | Offset(2) | Register |  | R/W | CLR |
| --- | --- | --- | --- | --- | --- |
| - | N/A | Port 3E Index | PP3EI7-0 | RW | P |
| 00h 01h 02h 03h 04h 05h 06h 07h 08h 09h 0Ah 0Bh 0Ch 0Dh 0Eh 0Fh 10h 11h 12h 13h 14h 15h 16h 18h 19h 1Ah 1Bh 1Ch 1Dh 1Eh 20h 21h 22h 23h 24h 25h 28h 29h 2Ah 2Bh 2Ch 2Dh 30h 31h 32h 33h | 800 801 802 803 804 805 806 807 808 809 80A 80B 80C 80D 80E 80F 810 811 812 813 814 815 816 818 819 81A 81B 81C 81D 81E 820 821 822 823 824 825 828 829 82A 82B 82C 82D 830 831 832 833 | Identification and Revision Interface Status Power Control Interrupt and General Control Card Status Change Card Status Change Interrupt Control Window Enable I/O Window Control I/O Window 0 Start Low Address I/O Window 0 Start High Address I/O Window 0 Stop Low Address I/O Window 0 Stop High Address I/O Window 1 Start Low Address I/O Window 1 Start High Address I/O Window 1 Stop Low Address I/O Window 1 Stop High Address Memory Window 0 Start Low Address Memory Window 0 Start High Address Memory Window 0 Stop Low Address Memory Window 0 Stop High Address Memory Window 0 Offset Low Address Memory Window 0 Offset High Address Additional General Control Memory Window 1 Start Low Address Memory Window 1 Start High Address Memory Window 1 Stop Low Address Memory Window 1 Stop High Address Memory Window 1 Offset Low Address Memory Window 1 Offset High Address Global Control Memory Window 2 Start Low Address Memory Window 2 Start High Address Memory Window 2 Stop Low Address Memory Window 2 Stop High Address Memory Window 2 Offset Low Address Memory Window 2 Offset High Address Memory Window 3 Start Low Address Memory Window 3 Start High Address Memory Window 3 Stop Low Address Memory Window 3 Stop High Address Memory Window 3 Offset Low Address Memory Window 3 Offset High Address Memory Window 4 Start Low Address Memory Window 4 Start High Address Memory Window 4 Stop Low Address Memory Window 4 Stop High Address | PPRVN7-0 PPIFS7-0 PPPCN7-0 PPICN7-0 PPCSC7-0 PPCSI7-0 PPWEN7-0 PPWCN7-0 PPI0S7-0 PPI0S15-8 PPI0E7-0 PPI0E15-8 PPI1S7-0 PPI1S15-8 PPI1E7-0 PPI1E15-8 PPM0S7-0 PPM0S15-8 PPM0E7-0 PPM0E15-8 PPM0O7-0 PPM0O15-8 PPACN7-0 PPM1S7-0 PPM1S15-8 PPM1E7-0 PPM1E15-8 PPM1O7-0 PPM1O15-8 PPGCN7-0 PPM2S7-0 PPM2S15-8 PPM2E7-0 PPM2E15-8 PPM2O7-0 PPM2O15-8 PPM3S7-0 PPM3S15-8 PPM3E7-0 PPM3E15-8 PPM3O7-0 PPM3O15-8 PPM4S7-0 PPM4S15-8 PPM4E7-0 PPM4E15-8 | RW R RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW RW | P - P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P P |

### PC-Card 16 Register – continued.

| Offset (1) | Offset (2) | Register |  | R/W | CLR |
| --- | --- | --- | --- | --- | --- |
| 34h 35h 3Bh 3Ch 3Eh | 834 835 83B 83C 83E | Memory Window 4 Offset Low Address Memory Window 4 Offset High Address ToPIC100 Card Timing Register Audio/Video Switching Register ToPIC100 Function Control Register | PPM4O7-0 PPM4O15-8 PPCTM7-0 PPAVS7-0 PPTFN7-0 | RW RW RW RW RW | P P P P P |

# NOTE:PC-Card 16 Register : Resume Clear can be executed by setting Power Control Register.

### CardBus Register

Base Address (10h/Device ID:0617h)

| Offset |  | NAME |  | R/W | CLR |
| --- | --- | --- | --- | --- | --- |
| 000h 004h 008h 00Ch 010h |  | Socket Event Socket Mask Socket Present State Socket Force Power Control | PPSE31-0 PPSM31-0 PPSS31-0 PPSF31-0 PPPC31-0 | R RW R W RW | P P P P P |

# ToPIC100 Configuration Register

7.1 	Vendor ID Register

Vendor ID Register maintains vendor ID.  Default value will be on after re-setting.

This register is Configuration Control Register (Config. offset: FCh): Write is enabled when ID Write Enable bit is 1b.

Configuration Control Register (Config. offset: FCh): The register is read only

when ID Write Enable

bit is 0b.

| Config | NAME | RW | D16 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 00h | PPVID | R |  |  | 1179h |

7.2 Device ID Register

Device ID Register maintains vendor ID.  Default value will be on after re-setting.

This register is Configuration Control Register (Config. offset : FCh) : Write is enabled when ID Write Enable bit is 1b.

Configuration Control Register (Config. offset : FCh) : The register is read only

when ID Write Enable bit is 0b.

| Config | NAME | RW | D31 | D16 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 02h | PPDID | R |  |  | 0617h |

7.3	Command Register

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 04h | PPCMD | RW | - | - | - | - | - | - | MFBE | SRRE | 0000h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | WCC | PERE | - | MWIE | SCE | BME | MAE | IOAE |  |

# D9:	 Fast Back-to-Back Enable bit

This field is fixed “0”. Because a master can not do fast back-to-back transactions

to  different devices.

D8:	 SERR# Enable bit

This is Enable bit for ToPIC100 to output SERR# signal to internal PCI bus

(Primary bus).

* ToPIC100 has no SERR# bin, and this bit has a meaning of set condition for Status Register-Signaled System Error bit (Config.Reg.06H-D14) .  Reset to 0b.

1b: When you get Parity Error in the address phase of access to ToPIC100 on internal PCI bus, ToPIC100 asserts SERR# onto the internal PCI bus. (It happens only when SERR# enable bit and Parity Error Response bit are active in both A  and b slots .)

ToPIC100 also asserts SERR# onto the internal PCI bus when System Error

Signal (CSERR#) on CardBus is active, but not onto the external PCI bus.

0b: ToPIC100 runs ignoring Parity Error in the address phase of access to ToPIC100 on the internal PCI Bus. ToPIC100 does not assert SERR# onto the internal PCI bus when System Error Signal

(CSERR#) on CardBus is active.

D7:	 Wait cycle control bit

This field is fixed “0”.  Because an address/data stepping is not supported.

D6:	 Parity Error Response bit

This is control bit that works to ToPIC100 when you get Parity Error in the access to ToPIC100 on the internal PCI bus (primary bus).  Reset to 0b.

1b: SERR#,PERR# Enable

0b:                                         Disable

ToPIC100 works as follows when you get Parity Errors in the access to ToPIC100 on the internal PCI Bus (primary bus).

Case 1 : Address phase – ToPIC100 asserts SERR# onto the internal PCI bus (primary bus) when both SERR# Enable bit (D8) and Parity Error Response bit (D6) for Config.Reg.04H are set in both A

and B slots.  It does not work unless eithr one is set, and can not assert SERR# on

to the external  PCI Bus.

Case 2 : Data phase  -  ToPIC100 asserts PERR# onto the internal PCI bus (primary

bus) when Parity Error Response bit (D6) is set in both A and B slots.  It does not

work unless either slot has Parity Error Response bit set.  Note that ToPIC100

does not have PERR pin, so it doesn’t assert PERR#.

D4:	 Memory Write and invalidate Enable bit

This field is fixed “0”.  Every memory write operation is carried out by the Memory

Write Command.

D3:	 Special Cycle bit

This field is fixed “0”.   Because a response to Special Cycle operation is not

supported.

D2:	 Bus Master Enable bit

Enable to act as a master on the PCI Bus and CardBus.

1:  Possible to act as a master on the PCI Bus and CardBus.

0:  Impossible to act as a master on the PCI Bus and CardBus.  Responds to the

access from PC card for CardBus by master-abort.

D1:	 Memory Access Enable bit

1:  Possible to respond to memory space accesses.

0:  Impossible to respond to memory space acceses.

D0:	 I/O access Enable bit

1:  Possible to respond to I/O space accesses.

0:  Impossible to respond to I/O space accesses.

## 7.4 	Status Register

Maintain status information of the internal PCI bus.

Read and write enabled bit becomes 0b by writing 1b.

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 06h | PPST | R | DPER | SSER | RMAB | RTAB | STAB | DVT1 | DVT0 | DPDT | 0490h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | FBBE | - | - | NCAP | - | - | - | - |  |

# D15:	     Detected Parity Error bit

This field is set to “1” if this controller detects a parity error when it acts as a master or a target on the PCI Bus.

D14:	     Signaled System Error bit

This field is set to “1” if this controller signal that it asserts SERR# on the PCI

Bus.

D13:	       Received Master Abort bit

This field is set to “1” if this controller terminates its transaction with master-abort when it acts as a master on the PCI Bus.

D12:	     Received Target Abort bit

This field is set to “1” if this controller is terminated its transaction by target-abort when it acts as a master on the PCI Bus.

D11:	     Signaled Target Abort bit

This field is set to “1” if this controller terminates a transaction with target-

abort when it acts as a master on the PCI Bus.

D10-D9:   DEVSEL# Timing

0 0: Fast

0 1: Medium

1 0: Slow

1 1: sub

D8:	     Data Parity Detected bit

This field is set to “1” by the following conditions.

- This controller asserted PERR#  itself or observed PERR# asserted.

- PERR#  asserted when this controller acts as a master on the PCI Bus.

- When Parity Error Response of Command Register (Config: 04h) is set to

“1”.

# D7:	     Fast Back-to-Back Capable bit (“1” fixed)

1:  Enable

0:  Disable

D4:	     New Capabilities

It shows if NOVA can implement the list for extended capabilities such as PCI Power Management.

1b: shows New Capabilities (list for PCI Power Management) exist.

(Implementation enabled.)

0b: shows New Capabilities (list for PCI Power Management) is not

implemented.

D15 – D11 and D8 are reset to “0” by writing “1”.

7.5 	Revision ID Register

Revision ID Register maintains Revision ID for ToPIC100.  Default value after reset.

Configuration Control Register  - ID Write Enable bit (Config. Reg.FCH-D0) =1b  write enabled.

= 0b   read only.

| Config | NAME | RW | D7 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 08h | PPRID | RW |  |  | 00h |

7.6 	Class Code Register

Class Code Register maintains Class Code for ToPIC100.  ToPIC100 is PCI Bridge

Device (06) which maps system resource (I/O, memory) to PC card, and works with

CardBus card (07).  The default value is 060700h.  Default  value  after reset.

Configuration Control Register－ID Write Enable bit (Config. Reg.FCH-D0)

= 1b    write enabled.

= 0b    read only

| Config | NAME | RW | D31 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 09h | PPCC | RW |  |  | 060700h |

7.7 	Latency Timer Register

ToPIC100 does not support Latency Timer and 00h fixed.

| Config | NAME | RW | D23 | D16 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 0Dh | PPLT | R |  |  | 00h |

7.8    Header Type Register

ToPIC100 is multi-functional device and PCI-to-CardBus bridge device, bit 7 and

bit1 are 1b.

| Config | NAME | RW | D23 | D16 | PCLR |
| --- | --- | --- | --- | --- | --- |
| 0Eh | PPHT | R |  |  | 82h |

7.9 	Base Address Register

| Config | NAME | RW | D31 |  |  | D12 | D11 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10h | PPBA | RW | BA31-12 |  |  |  | - |  | - | 0h |

# D31-D12:  Base Address

Sets up the base-address for mapping a Register-set of PC-Card16 and CardBus into the system resource.

The Register-set of PC-Card16 and CardBus is mapped into 4K byte memory fields from this base address.

The CardBus Register-set is mapped between 7FFh from 000h of the 4K Byte memory field. The PC-Card16 Register-set is mapped between FFFh from 800h of the 4K  memory  field. (The PC-Card16 Register-set is mapped at the head in the address  which added the offset value in PC-Card16 Regster to 800h.)

| Base Address | CardBus Register Set | Base Address+000h Base Address+7FFh |
| --- | --- | --- |
|  | PC-Card16 Register Set | Base Address+800h Base Address+FFFh |

7.10 	Capability Pointer Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 14h | CID | R | CPT7 | CPT6 | CPT5 | CPT4 | CPT3 | CPT2 | CPT1 | CPT0 | 80h |

# D7-D0:     Cap_Ptr

Cap_Ptr provides Offset in the NOVA’s PCI configuration field to the position of the first item (PCI Power Management registers) on the Capabilities Linked List.

In NOVA, double word on the PCI header in 80h and 84h are PCI Power

Management registers.

7.11 	Secondary Status Register

Secondary Status Register has similar functions to Status Register that is defined in the PCI Bus specification, however it shows the status for CardBus.  Secondary Status Register is different from Status register in 14bit Received System Error bit, which is Signaled System Error bit  in Status Register.

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 16h | PPCMD | RW | DPER | RSER | RMAB | RTAB | STAB | DVT1 | DVT0 | DPDT | 0480h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | FBBE | - | - | - | - | - | - | - |  |

# D15:	     Detected Parity Error bit

This field is set to “1” if this controller detect a parity error when it acts as a

master or a target on the CardBus.

D14:	     Received System Error bit

This field is set to “1” if this controller receive that SERR# is asserted on the

CardBus.

D13:	     Received Master Abort bit

This field is set to “1” if this controller terminates its transaction with master-abort when it acts as a master on the CardBus.

D12:       Received Target Abort bit									This fiels is set to “1” if this controller is terminated its transaction by target-

abort when it acts as a master on the CardBus.

D11:	     Signaled Target Abort bit

This field is set to “1” if this controller terminates a transaction with target-

abort when it acts as a target on the CardBus.

D10-D9:    DEVSEL# Timing

00b:  Fast

01b:  Medium

10b:  Slow

11b:  sub

# D8:	     Fast Back-to-Back Capable bit

This field is set to “1” by the following conditions.

- This controller asserted PERR# itself or observed PERR# asserted.

- PERR# asserted whe this controller acts as a master on the PCI Bus.

- When Parity Error Response of Bridge Control Register (config: 3Eh) is

set to “1”.

# D7:	     Fast Back-to-Back Capable bit (“1” fixed)

1: Enable

0: Disable

D15 – D11 and D8 are reset to “0” by writing “1”.

7.12 	PCI Bus Number Register

PCI Bus Number Register stores Bus Number of the internal PCI Bus (Primary Bus) connected to ToPIC100.

Configuration SoftWare configures PCI Bus Number Register.

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 18h | PPPBN | RW | BNO7 | BNO6 | BNO5 | BNO4 | BNO3 | BNO2 | BNO1 | BNO0 | 00h |

D7-D0:	PCI Bus Nmber

This register holds the number of the PCI Bus.

7.13 	Secondary Bus Number Register

Secondary Bus Number Register stores Bus Number of CardBus connected to ToPIC100.

Configuration SoftWare configures Secondary Bus Number Register.

ToPIC100 converts Type 1 configuration cycle on the internal PCI Bus into Type 0 configuration cycle on CardBus when the bus number matches to Secondary Bus Number Register.

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 19h | PPSCN | RW | CNO7 | CNO6 | CNO5 | CNO4 | CNO3 | CNO2 | CNO1 | CNO0 | 00h |

# D7-D0:	CardBus Bus number

This register holds the number of the CardBus attached to the socket.

7.14 	Subordinate Bus Number Register

The bus number of Type1 configuration cycle on the internal PCI Bus is larger than Secondary Bus Number Register.  When the bus number is smaller than Subordinate Bus Number Register AND the davice number of Type1 configuration cycle is 0_0001b, ToPIC100 converts Type1 configuration cycle on to CardBus.

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Ah | PPSBN | RW | SNO7 | SNO6 | SNO5 | SNO4 | SNO3 | SNO2 | SNO1 | SNO0 | 00h |

# D7-D0:	Subordinate CardBus Bus Number

This register holds the numebr of the CardBus at the lowest part of the

hierarchy  when the CardBus attached hierarchically.

7.15 	1st Memory window Base Register

1st Memory window Base Register shows the start address that needs to have Memory

Access on the internal  PCI Bus execute on the 1st-Memory-window on CardBus.  It gets expired when the superordinate 20 bit of 1st Memory window Limit Register(Config. offset : 20h) is all0b. (Address Decode does not execute.)

| Config | NAME | RW | D31 |  |  |  | D12 | D11 |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Ch | PP1MB | RW | AD31 |  |  |  | AD12 | - |  |  | 00000h |

The upper 20 bits define AD<31:12> on CardBus.

The lower 12 bits are set to 0b fixed.

The memory space is given on CardBus on a 4K bite boundary by this register and 1st Memory window  Limit  Register(Config. offset : 20h).

D31-D12:     	1st Memory Window Start Address

This register holds a base address for forwarding a memory transaction on the

PCI Bus to the CardBus.

It defines AD31-12 on the CardBus.  The lower 12 bits are all 000h.

The memory space of the Card Bus is starting on a 4K boundary.

7.16	1st Memory window Limit Register

1st Memory window Limit Register shows the limit address that needs to have Memory Access on the internal PCI Bus execute on 1st-Memory-window on CardBus.

ToPIC100 does not respond to Memory Access to CardBus for the 1st-Memory-window (Address Decode does not execute) when the superordinate 20 bit is all0b.

| Config | NAME | RW | D31 |  |  |  | D12 | D11 |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 20h | PP1ML | RW | AD31 |  |  |  | AD12 | - |  |  | 00000h |

The upper 20 bits define AD<31:12> on CardBus.

The lower 12 bits are set to 1b fixed, but they are all set to 000h when a read access.

The memory space is given on CardBus on a 4K bite boundary by this register and 1st Memory window Base Register (Config. offset : 1Ch).

# D31-D12:  	1st Memory Window Limit Address

This register holds a limit address for forwarding a memory transaction on the

PCI Bus to the CardBus.

It defines AD31-12 on the CardBus.  The lower 12 bits are all fixed FFFh, but they

are all set to 000h when a read access.

If the AD31-12=00000h, any memory access is not accepted.

7.17	2nd Memory window Base Register

2nd Memory window Base Register shows the start address of the address range that needs to have Memory Access on the internal PCI Bus execute on 2nd Memory-window on CardBus.

It gets expired when the superordinate 20 bit of 、2nd Memory window Limit Register(Config. offset : 28h)  is all0b. (Address Decode does not execute.)

| Config | NAME | RW | D31 |  |  |  | D12 | D11 |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24h | PP2MB | RW | AD31 |  |  |  | AD12 | - |  |  | 00000h |

The upper 20 bits define AD<31:12> on CardBus.

The lower 12 bits are set to 0b fixed.

The memory space is given on CardBus on a 4K bite boundary by this register and 2nd Memory window Limit Register(Config. offset : 28h).

# D31-D12:	2nd Memory Window Start Address

This register holds a base address for forwarding a memory transaction on the PCI Bus to the CardBus.

It defines AD31-12 on the CardBus.  The lower 12 bits are all 000h.

The memory space on the CardBus is starting on a 4K boundary.

7.18 	2nd Memory window Limit Register

2nd Memory window Limit Register shows the limit address of the address range that needs to have Memory Access on the internal PCI Bus execute on 2nd Memory-window on CardBus.

ToPIC100 does not respond to Memory Access to CardBus for the 2nd-Memory-window when the superordinate 20 bit is all0b. (Address Decode does not execute)

| Config | NAME | RW | D31 |  |  |  | D12 | D11 |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 28h | PP2ML | RW | AD31 |  |  |  | AD12 | - |  |  | 00000h |

The upper 20 bits define AD<31:12> on CardBus.

The lower 12 bits are set to 1b fixed, but they are all set to 000h when a read access.

The memory space is given on CardBus on a 4K bite boundary by this register and 2nd Memory window Base Register(Config. offset : 24h).

# D31-D12:	2nd Memory Window Limit Address

This register holds a limit address for forwarding a memory transaction on the

PCI Bus to the CardBus.

It defines AD31-12 on the CardBus.  The lower 12 bits are all FFFh, but they are

all set to 000h when a read access.

If the AD31-12=00000h, any memory access is not accepted.

7.19	1st I/O window Base(Lower) Register

| Config | NAME | RW | D15 |  |  |  |  | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Ch | PP1IBL | RW | AD15 |  |  |  |  | AD2 | - | - | 0000h |

# D15-D2:	1st I/O Window Start Address

This register holds a lower 16 bits of a base address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

It defines AD15-2 on the CardBus.  The lower 2 bits of this register are all set to

00b.

The I/O space on the Card Bus is starting on a 4K boundary.

7.20   1st I/O window Base(Upper) Register

| Config | NAME | RW | D15 |  |  |  |  |  |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Eh | PP1IBU | R | AD31 |  |  |  |  |  |  | AD16 | 0000h |

D15-D0:	1st I/O Window Start Address (“0000h fixed”)

This register holds a upper 16 bits of a base address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

This conrtoller supports the I/O space in 64K, and this register is fixed “0000h”.

It defines AD31-16 on the CardBus.

7.21	1st I/O window Limit(Lower) Register

| Config | NAME | RW | D15 |  |  |  |  | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 30h | PP1ILL | RW | AD15 |  |  |  |  | AD2 | - | - | 0000h |

# D15-D2:	1st I/O Window Stop Address

This register holds a lower 16 bits of a limit address for fowarding a I/O

transaction on the PCI Bus to the CardBus.

It defines AD15-2 on the CardBus.  The lower 2 bits of this register are set to 11b.

It the AD15-2=0000h, any I/O access is not accepted.

7.22 	1st I/O window Limit(Upper) Register

| Config | NAME | RW | D15 |  |  |  |  |  |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 32h | PP1ILU | R | AD31 |  |  |  |  |  |  | AD16 | 0000h |

D15-D0:	1st I/O Window Stop Address (“0000h” fixed)

This register holds a upper 16 bits of a limit address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

This conrtoller supports the I/O space in 64K, and this register is fixed “0000h”.

It defines AD31-16 on the CardBus.

7.23 	2nd I/O window Base(Lower) Register

| Config | NAME | RW | D15 |  |  |  |  | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34h | PP2IBL | RW | AD15 |  |  |  |  | AD2 | - | - | 0000h |

# D15-D2:	2nd I/O Window Start Address

This register holds a lower 16 bits of a base address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

It defines AD15-2 on the CardBus.  The lower 2 bits of this register are set to

“00b”.

The I/O space on the CardBus is starting on a 4K boundary.

7.24	2nd I/O window Base(Upper) Register

| Config | NAME | RW | D15 |  |  |  |  |  |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 36h | PP2IBU | R | AD31 |  |  |  |  |  |  | AD16 | 0000h |

D15-D0:	2nd I/O Window Start Address (“0000h” fixed)

This register holds a upper 16 bits of a base address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

This conrtoller supports the I/O space in 64K, and this register is fixed “0000h”.

It defines AD31-16 on the CardBus.

7.25 	2nd I/O window Limit(Lower) Register

| Config | NAME | RW | D15 |  |  |  |  | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 38h | PP2ILL | RW | AD15 |  |  |  |  | AD2 | - | - | 0000h |

# D15-D2:	2nd I/O Window Stop Address

This register holds a lower 16 bits of a limit address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

It defines AD15-2 on the CardBus.  The lower 2 bits of this register are set to

“11b”.

If the AD15-2=0000h, any I/O access is not accepted.

7.26	2ndI/O window Limit(Upper) Register

| Config | NAME | RW | D15 |  |  |  |  |  |  | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Ah | PP2ILU | R | AD31 |  |  |  |  |  |  | AD16 | 0000h |

D15-D0:	2nd I/O Window Stop Address (“0000h” fixed)

This register holds a upper 16 bits of a limit address for forwarding a I/O

transaction on the PCI Bus to the CardBus.

This conrtoller supports the I/O space in 64K, and this register is fixed “0000h”.

It defines AD31-16 on the CardBus.

7.27	Interrupt Line Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Ch | PPITRL | RW | IL7 | IL6 | IL5 | IL4 | IL3 | IL2 | IL1 | IL0 | 00h |

# D7-D0:	Interrupt level bit

The initialization program holds this bit.

Device drivers and OS read the value on demand.

7.28	Interrupt Pin Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Dh | PPITRP | R | - | - | - | - | - | - | IPS1 | IPS0 | 00h |

D7-D2:	Reserved

0b : fixed

D1-D0:		Interrupt Pin select bit

These fields assign the data holded in the Interrupt Control Registe - Interrupt Pin

Assign bit  (Config. offset : A1h-D4,D5).

0 0b :  Disable

0 1b :  Interrupt assigned to INTA.

1 0b :  Interrupt assigned to INTB.

11b :  Reserved.

7.29	Bridge Control Register

Bridge Control Register is expanded Command Register for PCI-CardBus Bridge

specifications.

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Eh | PPBCN | RW | - | - | - | - | - | WBEN | M1PE | M0PE | 0300h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | INTE | CBRS | MSAM | - | VGAE | ISAE | SERR | PERE |  |

# D10	Write Buffer Enable bit

1b : Enable

Write buffers are enabled.

0b : Disable

D9:	Memory 1 Prefetch Enable bit

1b : Enable

Pre-fetch operation is carried out when a memory read transaction to

the 2nd  Memory  Window space.

0b : Disable

D8:	Memory 0 Prefetch Enable bit

1b : Enable

Pre-fetch operation is carried out when a memory read transaction to

the 1st  Memory  Window space.

0b : Disable

D7:	IREQ-INT Enable bit

1b :  Enable

The interrupt signal from Card (BSYAZ/BSYBZ) is assigned to one of

the serial  interrupts signals (IRQ 3-15) in case of PC Card16/CardBus.

The assignment is determined according to D3-0 of Interrupt and

General Control  Register (Offset : 03h).

0b :  Disable

The interrupt signal from Card (BSYAZ/BSYBZ) is assigned to

INTAZ/INTB in case of  PC-Card16/CardBus.

The assignment is determined according to D5 – 4 of Interrupt

Control Register  (Offset : A1h).

D6:        	CardBus Reset Enable

1b: Enable

CRST# is enable to assert on the CardBus.

0b: Disable

D5:	Master Abort Mode bit

This field control to signal a target abort during a master abort asserted.

1b: Possible t signal a target abort

0b: Impossible to signal a target abort.

D3:	       VGA Enable bit

1b : Enable

Possible to forward a transaction of VGA on the PCI Bus to the CardBus through

the I/O spcae   (3Boh – 3BBh, 3Coh – 3DFh) and the memory space (A0000h –

BFFFFh).

But a transaction to the PCI Bus from the CardBus is inhibited by a master abort.

Configuration Register (in which I/O space and memory space and ISA enable are

set up) is  ineffective at this condition.

0b : Disable

D2:	     ISA Enable bit

1b : Enable

In the access to the CardBus from the PCI Bus, the transaction is forwarded to

the lower 256  bytes of I/O space of the 1K-byte unit defined by the I/O window

BaseXX register – the I/O  window LimitXX register of a Configuratoin.

In the access to the PCI Bus from the CardBus, the transaction is forwarded to

the upper 768  bytes of I/O space of the 1K-byte unit defined by the I/O window

BaseXX register – the I/O   window LimitXX register of a Configuration.

0b : Disable

The transaction is forwarded to the I/O space defined by the I/O window BaseXX Register – the

I/O window LimitXX Register.

D1:	     SERR# Enable bit

0b : Disable

1b : Enable

SERR#  signaled on the CardBus is related to D14 of status Register (Config : 06h), only when the D8 of Command Register (Config : 04h) is set to “1”.

D0:	     Parity Error Response Enable bit

0b : Disable

1b : Enable

Possible to signal and detect an address/data parity error signaled on the

CardBus.

7.30  Subsystem Vendor ID Register

Configuration Control Register(Config. offset : FCh) : ID Write Enable bit

1b : Write enable

0b : Write disable – read only.

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 40h | PPSVID | RW | SV15 | SV14 | SV13 | SV12 | SV11 | SV10 | SV9 | SV8 | 1179h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | SV7 | SV6 | SV5 | SV4 | SV3 | SV2 | SV1 | SV0 |  |

# D15-D0:	Subsystem Vendor ID bit

## Subsystem Device ID Register

Configuration Control Register(Config. offset : FCh) : ID Write Enable bit

1b : Write enable

0b : Write disable – read only.

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 42h | PPSDID | RW | SD15 | SD14 | SD13 | SD12 | SD11 | SD10 | SD9 | SD8 | 0001h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | SD7 | SD6 | SD5 | SD4 | SD3 | SD2 | SD1 | SD0 |  |

# D15-D0:     System Device ID bit

## PC Card16 Legacy Mode Base Address Register

| Config | NAME | RW | D31 |  |  | D16 | D15 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 44h | PPLMB | RW | - |  |  |  | LMB15-1 |  | 1 | 01h |

# D15-D1:    PC Card16 Bit IF Legacy Mode Base Address Bit

# This register holds a base address with Legacy Mode when Card Detect

# control Register   (Config : A3h) is set to “0”.

# Supports a Legacy Mode operation with non-zero address.

D0:         Reserved.

1b : fixed.

## Capability ID Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 80h | NVCID | R | CID7 | CID6 | CID5 | CID4 | CID3 | CID2 | CID1 | CID0 | 01h |

# D7-D0:    	Cap_ID

# 01h : Shows the Items are PCI Power Management registers.

## Next Item Ptr Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 81h | NVNIPTR | R | NIP7 | NIP6 | NIP5 | NIP4 | NIP3 | NIP2 | NIP1 | NIP0 | 00h |

# D7-D0:     Next_Item_Ptr

# Assign Offset in PCI configuration space to Next Item.

# Set to 00h.

## Power Management Capabilities (PMC) Register

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 82h | NVPMC | R | PME4 | PME3 | PME2 | PME1 | PME0 | D2SP | D1SP | - | FE11h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | - | - | DSI | VAPS | PMEC | VER2 | VER1 | VER0 |  |

# D15-11:    PME_Support

0b : PME# is not asserted at corresponded power state.

D15 – 0b : Vaux is not supported.

D15:	     1XXXXb:  	PME# is asserted from D3cold.  Set to 1b fixed.

D14:	     X1XXXb: 	 PME# is asserted from D3hot.   Set to 1b fixed.

D13:	     XX1XXb:	PME# is asserted from D2.  Set to 1b fixed.

D12:	     XXX1Xb:	PME# is asserted from D1.  Set to 1b fixed.

D11:	     XXXX1b:	PME# is asserted from D0.  Set to 1b fixed.

D10:	     D2 Support

Set to “1” fixed.

1b:  Power Management State of D2 is supported.

D9:	     D1 Support

Set to “1” fixed.

1b:  Power Management State of D1 is supported.

D8-D6:     Reserved

Set to “000b” fixed.

D5:	     DSI(Device Specific Initialization)

Set to “0” fixed.

D4:	     Auxiliary Power Source(VAUX)

This field is effective only when D15 is 1b.  Set to “1” fixed.

1b: To support PME# in D3cold, auxiliary power supplied via proprietary

transmission  path is needed.

0b: This controller itself supplies auxiliary power.

D3:	     PME Clock

Set to “0” fixed.

1b: PME# operation is affected by with or without PCI clock.

0b: PCI clock is not needed to generate PME#.

D2-0:	     Version

Set to “001b” fixed.

001b: This controller is ‘The Revision 1.0 of the PCI Power Management

Interface Specification’ compliant.

## Power Management Control/Status (PMCSR) Register

| Config | NAME | RW | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 84h | NVPMCS | RW | PMES | DSC1 | DSC0 | DSL3 | DSL2 | DSL1 | DSL0 | PMEE | 0000h |
|  |  | /R | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | - | - | - | - | - | - | PST1 | PST0 |  |

D15:	     PME status (Read only)

1b:  This field is set to “1” when this controller assert PME#.  It is

independent from the status of PME_En(D8).

Invalid when writing 0.

D14-13:    Data scale(Read only)

00b:	Unknown

01b:	0.1x [W]

10b:	0.01x [W]

11b:	0.001x [W]

D12-9:	     Data select

0000b:	Electric power consumption for D0.

0001b:	Electric power consumption for D1.

0010b:	Electric power consumption for D2.

0011b:	Electric power consumption for D3.

0100b:	Heat loss for D0.

0101b:	Heat loss for D1.

0110b:	Heat loss for D2.

0111b:	Heat loss for D3.

1000b:	Electric power consumption for the common logic.

D8:	     PME_En

This fieled has to be cleared explicitly by OS when it is loaded.

1b:	Enable.  This controller asserts PME#.

0b:	Disable.  This controller is not able to assert PME#.

D7-D2:     Reserved (Read only)

Set to “000000b” fixed.

D1-0:	     PowerState

This field determines current power state of this controller and holds new power state.

However, when writing given power state which the transition at each power stae is not permitted, write operation ends normally, but the transition of the power state does not take place with the data disregarded.

00b:	D0

01b:	D1

10b:	D2

11b:	D3hot

## PMCSR PCI to CardBus Bridge Support Extensions Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 86h | NVPPCBS | R | BPCC | B2B3 | - | - | - | - | - | - | 80h |

D7:	     Bus Power/Clock Control Enable (Read only)

Set to “1” fixed.

1b :	Bus Power/Clock Control mechanism is valid.

0b :	Bus Power/Clock Control mechanism is invalid.

In this case, System Software is not able to use PowerState bit (D1-D0)

of PMCSR  Register(Config. offset : 84) with the purpose of

controlling power or clock.

D6:	     B2_B3#(B2/B3 support for D3hot) (Read only)

This field defines behevior resulted directly from this controller being programmed by D3hot. It is valid only when when D7 is “1”.

Set to “0” fixed.

1b :	NOVA stops the clock to Secondary Bus when D3hot. (B2)

0b :	NOVA stops the clock to Secondary Bus when D3hot , and it becomes defeasible for the power to Secondary Bus. (B3)

D5-D0:     Reserved (Read only)

Set to “000000b” fixed.

## Data Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 87h | NVDATA | R | - | - | - | - | - | - | - | - | 00h |

D7-D0:     Reserved (Read only)

Set to “00h” fixed.

7.38 	CardBus Socket Power Detect Control Register

This field holds the interval after the output of control signal for the card electric power when inserting the card.

It starts identifying the card after the card electric power is stabilized.

| Config | NAME | RW | D31 |  |  |  |  |  |  | D16 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 90h | PPCSPDC | RW |  |  |  |  |  |  |  |  | 0000h |
|  |  | /R | D15 |  |  | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | - | - | - | - | - | -PST2 | PST1 | PST0 |  |

D31-3:	     Reserved (Read only)

Set to “00000000h” fixed.

D2-0:		     Power Detect Timing bit

This field controls wait timings of power supply.

000b: 2 ms wait

001b: 4 ms wait.

010b: 8 ms wait.

110b: 16 x PCICLK

111b: 4 x PCICLK

others: Reserved

## ZV Control Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 9Ch | PPZVC | RW | - | - | - | - | - | - | - | ZVCN | 00h |

# D0:	     ZV Control bit

1b : ZV Enable

AUDIO/VIDEO ZV port function is enabled.

0b : ZV Disable

Possible to read a status of ZV port when D1 of MISC2 Register (Config : AEh) is set to “1”.

This bit is set to “1” if ZV port is used.

It changes when D1 or D0 of Audio/Video switching Register (Offset : 3Ch) is changed, since they are related to each other.

This is Audio/Video in common, it is set to “1” when either one of Card16 Reg.3Ch D1 or D0 is “1”.

## Slot Control Register

Each slot has many control/status register sets. This register controls enable/disable in each slot and allocation of I/O port, etc.

Note : Some registers have been added or changed based on Intel82092 (PPEC) in this controller.

This register is PC-Card 16 PCMCIA Slot Control Register compatible.

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A0h | PPSLT | RW | ESLT | EREG | EHDN | IDWP | PAD1 | PAD0 | OFS1 | OFS0 | 00h |

# D7:	     SLOTON bit

1b : Enable

CardBus slot function is enabled.

0b : Disable

No response to the access for PC-Card16 register and CardBus register.

D6:	     SLOTEN bit

1b : Enable

The access to the register-set of PC-Card16 and CardBus is enabled.

0b : Disable

D5:	     ID_LOCK bit

This bit controls write access to the following registers.

Card16 Reg. 3Bh : ToPIC100 Card Timing Register

3Eh : ToPIC100 Function Control Register

3Fh : Toshiba Hidden Register

1b : LOCK (Disable)

The write access to Toshiba hidden Register (Offset : 3Fh) is enabled.

0b : UNLOCK (Enable)

D4:	     ID_WP bit

1b : Write Protect

The write access to ID & Revision Register (Offset : 00h) is enabled.

0b : Write Enable

D3-D2:     Slot Port Select bit

This bit is valid when PC-Card16/32 mode Select bit in Card Detect Control Register (Config. offset : A3h) is “0”.

00b : Index port 3E0h / Data port 3E1h

01b : Index port 3E2h / Data port 3E3h

10b : Index port 3E4h / Data port 3E5h

11b : Index port 3E6h / Data port 3E7h

D1-D0:     Offset Select bit

This bit is valid when PC-Card16/32 mode Select bit in Card Detect Control Register (Config. offset : A3h) is “0”.

00b : 00h - 3Fh

01b : 40h - 7Fh

10b : 80h - BFh

11b : C0h – FFh

## Interrupt Control Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A1h | PPIRC | RW | - | - | IPA1 | IPA0 | - | STIQ | IRPL | IRLN | 00h |

# D5-D4:     Interrupt Pin Assign bit

These fields assign an interrupt to an external output signal .

00b : Disable

01b : Assign an interrupt to INTA

10b : Assign an interrupt to INTB

11b : Reserved

D2:	     STSIRQNP bit

This field set up an output mode of a status change interrupt.

1b : Pulse mode

0b : Through mode

# D1:	     IRQNP bit

This field set up an output mode of an IRQ interrupt.

1b : Pulse mode

0b : Through mode

# D0:	     IRQ/INT select bit

0b: IRQ selected

The status change interrupt (BVDAZ / BVDBZ) from Card is assigned to INTAZ /

INTBZ in case of PC-Card 16.

The assignment is determined according to D3 – 0 of Interrupt & General Control

Register (Offset : 03h)

1b: INTA Selected

The status change interrupt (BVDAZ/BVDBZ) from Card is assigned to

INTAZ/INTBZ is case of PC- Card16.

The assignment is determined according to D5 – 4 of Interrupt Control Register

(Config : A1h)

## Card Detect Control Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A3h | PPCDT | RW | PCMD | - | - | - | - | VSS1 | VSS0 | DMSL | 00h |

# D7:	     PC-Card16/32 mode Select bit

1b : PC-Card16 / CardBus mode

0b : PC-Card16 mode (Default)

D2-D1:     Voltage Sense Pin enable bit

The external output signal VS2AZ / VS2BZ and VS1AZ / VS1BZ are enabled when a Card is detected by software (D0 of this register is set to “1”.)

11b : VS2=Hi-Z, VS1 = Hi-Z (Default)

10b : VS2=Hi-Z, VS1 = LOW

01b : VS2=LOW, VS1 = Hi-Z

00b : VS2=LOW, VS1 = LOW

D0:	     Detect Method Select bit

This bit determines software / hardware to detect a card.

1b :  A card is detected by software.

0b : A card is detected by hardware. (Default)

## CardBus Socket Register Control Register

| Config | NAME | RW | D31 | D30 | D29 | D28 | D27 | D26 | D25 | D24 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A4h | PPSRC | RW | RRE | CRRE | CKRN | CTST | IOPU | CRSE | SSPO | SSSO | 0Ch |
|  |  |  | D23 |  |  | D16 | D15 D11 | D10 | D8 | PCLR |
|  |  |  | - |  |  | CBRE | CDD4-0 | - |  | 0000h |
|  |  |  | D7 |  |  |  | D3 | D2 | D1 | D0 | PCLR |
|  |  |  | - |  |  |  |  | DRI | CAOF | CAIE | 00h |

# D31:	     Resume Reset Enable bit

1b: Enable

The CardBus Register-set are reset when resumed.

0b: Disable

The CardBus Register-set are kept when resumed.

D30:	     CardBus Card Removal Reset Enable bit

1b: Enable

The CardBus Register-set are reset when CardBus is removed.

0b: Disable

D29:	     CLKRUNEN bit

1b: Enable

The CLKRUN function of CardBus is enabled.

It has priority over Stop Clock bit (CB Reg.010h－D7) of Power Control Register.

0b: Disable

D28:	     H256PCTE bit

1b: Test mode

The 256PCICLK counter is used as 16PCICLK counter.

0b: Normal mode

D27:	     IOPLUP bit

1b: The IO cell in the CardBus side are pulled up.

0b: Normal mode. (IO cell are not pulled up)

D26:	     CardBus Reset Control bit

0b:  Normal compatible mode (0 x PCICLK)

1b: 256 x PCICLK mode

D25:	     SUSPEND Socket Power Off bit

1b: Power to the socket is turned off in case of suspend mode.

0b: Power to the socket is supplied in case of suspend mode.

D24:	     SUSPEND Socket Signal Off bit

1b: Signal to the socket is set to “Hi-Z” in case of suspend.

0b:Signal to the socket is output in case of suspend.

D16:	     CardBus Register Write Enable Mode bit

0b: Invalidate bite enable

1b: Validate bite enable.

D15-D11:     CardBus Device Number bit

This field holds the CardBus Device Number.

D2:	       RIOUTDIS bit

Disable bit to RIOUT signal

1b: Disable

0b: Enable

D1:	       CAUDIO Signal Off bit

1b: CAUDIO signal input is invalid. (No input)

0b: Input CAUDIO signal.

D0:	     CAUDIO Invert Enable bit

1b: Enable

CAUDIO signal input is inverted.

0b: Disable

| PC Card Type | CAOF CAIE | AUDIO |
| --- | --- | --- |
| CardBus | 0 0 0 1 | CAUDIO ~CAUDIO |
| PC-Card16 | 0 0 0 1 | 0 1 |
| X | 1 0 1 1 | 0 1 |

7.44 	Wake Up Control Register

| Config | NAME | RW | D31 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| A8h | P PWUC | RW | - | RPOS | EC2W | EC1W | EB3W | EB2W | EB1W | EB0W | 00h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
|  |  |  | ESRW | EICW | EITW | ECSW | ESPS | ECLK | ECHG | SCHG | 00h |

# D31-D15:	Reserved (RW possible)

D14:		RI_OUT/PME# Pin Output Select

1b : Output RI_OUT from RI_OUT/PME# Pin.

0b : Output PME# from RI_OUT/PME# Pin.

# D13:		CCD2# Pin WakeUp Enable

1b : Enable

Wake-Up Event by CCD2# Pin is enabled.

0b : Disable

# D12: 		CCD1# Pin WakeUp Enable

1b : Enable

Wake-Up Event by CCD1# Pin is enabled.

0b : Disable.

# D11: 		Socket Event Register PowerCycle bit WakeUp Enable

1b : Enable

Wake-Up by Power Cycle bit of CB Register Socket Event Register is

enabled.

0b : Disable.

# D10: 		Socket Event Register CCD2# bit WakeUp Enable

1b : Enable

Wake-Up by CCD2# bit of CB Register Socket Event Register is enabled.

0b : Disable

# D9: 		Socket Event Register CCD1# bit WakeUp Enable

1b : Enable

Wake-Up by CCD1# bit of CB Register Socket Event Register is

enabled.

0b : Disable.

# D8: 		Socket Event Register CSTSCHG bit WakeUp Enable

1b : Enable

Wake-Up by CSTSCHG bit of CB Register Socket Event Register is

enabled.

0b : Disable

# D7: 		R2 STSCHG# Pin WakeUp Enable

1b : Enable

Wake-Up by R2 STSCHG# Pin is enabled.

0b : Disable

# D6: 		R2 IREQ# Pin WakeUp Enable

1b : Enable

Wake-Up by R2 IREQ# Pin is enabled.

0b : Disable

# D5: 		CB CINT# Pin WakeUp Enable

1b : Enable

Wake-Up by CB CINT# Pin is enabled.

0b : Disabled

# D4: 		CB CSTSCHG Pin WakeUp Enable

1b : Enabled

Wake-Up by CB CSTSCHG Pin is enabled.

0b : Disable

# D3:		Socket Present Status Register Clear Enable

1b : Enable

Socket Present Status Register is cleared by Card removal in case of

Suspend mode.

0b : Disable

# D2:		CLK32 Socket Event Register Enable

1b : Enable.

Socket Event Register with CLK32 is used.

D7 – D4 is enabled.

0b : Disable.

# D1:		STSCHG Output Enable

# This bit is related to D8 (PEM_EN) of Power Management Control/Status (PMCSR) Register (Config. offset : 84h). Writing to D8 of Power Management Control/Status (PMCSR) Register reflects this bit.

# This controller has no usual STSCHG pin.  RI_OUT/PME# Pin outputs STSCHG when D14 of this register is “0”.

1b : Enable

Internal output signal PCSTCG is enabled.

External output signal STSCHGZ is enabled (set to “L”) when D4 of

Enable Register (I/O : 00EFh, index : 6Ch) is “1”.

0b : Disable

# D0:		STSCHG Status

# This field indicates condition of external output signal STSCHG.

# It is reset to “0” when written “1”.

# This bit is related to Power Management Control/Status (PMCSR)

# Register (Config. offset : 84h)-D15(PME status).

# This bit is cleared when written “1” in the Register.

7.45 	Serial Interrupt Control Register

This register exists only one in this controller that controls Serial Interrupt and changes serial mode.

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ACh | PPSIC | RW | VSST | CMS | VSIS | VSOS | VSSM | VSIM | SICM | 00h |

D7:		VESA Serial Interrupt Status Bit (Read only)			(R_STATE)

0b: Continuous Mode

1b: Quiet Mode

D6:		Continuous Mode Select Bit 				              (R_CMODE)

0b: Carry breaking edge of the interrupt .

1b: Carry interrupt level in the Continuous Mode.

D5-4:		VESA Serial Interrupt Input Mode Select Bit 			   (R_INFF)

00b: Fetch serial interrupt signal when PCICLK. is rising.

01b: Fetch serial interrupt signal when PCICLK is breaking.

10b: Fetch serial interrupt signal 5ns after PCICLK rose.

D3:		VESA Serial Interrupt Output Mode Select Bit  	               (R_OUTFF)

0b: Output in sync with PCICLK rising.

1b: PCICLK in sync with PCICLK breaking.

D2:		VESA Serial Interrupt SMI Mapping Bit

0b:Direct output mode.

1b: Interrupt signal is output from Serial interrupt signal.

D1:		VESA Serial Interrupt INT Mapping Bit

0b: Direct output mode.

1b: Interrupt signal is output from Serial interrupt signal.

D0:		Serial Interrupt Control Mode Select Bit 		          (R_SIRQMOD)

0b: Toshiba method. (Default)

1b: VESA method.

7.46	MISC1 Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ADh | PPM1S | RW | CLKP | CLKM | - | DEMD | - | CSNC | - | RDLE | 01h |

D7:	     CLOCKRUN  Control bit (CLKRUNCNT)

1b : Enable

CLOCKRUNP protocol in PCI side is enabled.

0b : Disable

D6:	    CLOCKRUN mode bit (CLKRUNMOD)

1b : Clock input is always requested when CardBus Card is inserted.

0b : Clock input is requested only when a transaction is not finished.

D5:	    IRQ REQ mode bit

1b: Enable

CLOCKRUN is requested by interruption.

0b : Disable

D4:	    Detect REQ mode bit

1b : Enable

CLOCKRUN is requested by an interruption while detecting a Card.

0b : Disable

D3:	      EXT INT PASS mode bit

1b : Direct input mode

0b : Synchronized input mode

D2:	    CardBus Socket Present Register Not clear

1b : Disable (Conventional compatible mode)

0b : Enable

CardBus Socket Present Register is initialized.

D1:	    CardBus Buffer Control bit (CBBUFCNT)

1b : Buffer is turned on when CardBusCard is inserted.

0b : Buffer is turned on when CardBus Card is inserted and power supply to

the card is finished.

D0:	    R2 Data Bus Low Enable bit

1b : Assert Data Bus to Low when not RW access.

0b : Conventional compatible mode.

7.47	ZV Configuration Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AEh | PPM2S | RW | ZVPMS | - | - | - | - | - | ZVMD | R_ZVENZ | 00h |

D7:	    ZV Port Mode Select.

1b : Bus method.

0b : Multiplexer method.

D1:	    ZV Mode Select

1b : This field enable for indicating the status of ZV Port/

D0 of ZV Control Register (Config : 9Ch) and D1 – D0 of Audio /Video Switching Register

(Offset : 3Ch) indicate the status  of ZV Port when read..

0b : This field disable for indicating the status of ZV Port/

D0:           R_ZVENZ

1b : DISABLE

Write to 9Ch bit0 , 3Ch bit0, or1 have no sense.

0b : ENABLE

Value is written in the register by writing “1” to 9Ch bit0 , 3Ch bit0 and 1.

7.48	Buffer Control Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| B0h | PPBFC | RW | - | - | - | - | WBCS3 | WBCS2 | EPLTE | IPLTE | 07h |

D7:	    Reserved

“1” fixed.

D6-D4:    Reserved

“0” fixed.

D3-D2:    Write Buffer Count Select bit

00b : 4 counts    01b : 8 counts  1x" : 10 counts

NOTE: Default is 8 counts

D1:	    EPLT Enable bit

1b : Latency Timer enable.

(MWLT1, MWLTB, MRLT1, MRLTB, DBULT are enabled.)

Delay transaction and post are enabled.

0b : Latency Timer disable.(Direct mode)

Re-try is not returned to the master until the cycle for the target is

completed.

# D0:	    IPLT Enable bit

1b : Latency Timer enable. (DBDLT is enabled.)

Delay transaction and post are enabled.

0b : Latency Timer disable. (Direct mode)

Retry is not returned to the master until the cycle for the target

is completed.

Two kinds of Timer Start signal for disregarding flag to PCI.

NOTE: Timer counts re-try.

## Debug Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BBh | PPDBG | RW | - | CRCAE | RRCAE | ACMPT | - | - | GPORT | WTCH | 00h |

# D7:	Reserved

“0” fixed

D6:	CB Register Config Access Enable Bit

1b : Enable

CardBus Register is mapped in the configuration space.

Function number of config. Access is  ”4” in Slot A and ”5” in Slot B.

0b : Disable

D5:	R2 Register Config Access Enable Bit

1b : Enable

R2 Register is mapped in the configuration space.

Function number of config. Access is  ”6” in Slot A and ”7” in Slot B.

0b : Disable

D4: 	R2 Access Compatible Register

1b : IO/memory access to R2 Card timing is the same as existing model of this

controller.

0b : IO/memory access to R2 Card timing is the least spec of PCCard16. (Fast

access mode)

D3-D2:	Reserved

“0” fixed..

D1:	GPORT bit

1b:ZVPCLK=HI

0b:ZVPCLK=LOW

D0:	WATCH bit

1b:Internal signal trace mode

0b:Normal mode

NOTE : R2 Card can not be used when “1”.

===Internal signal and ZV output===

ZVPCLK	= GPORT

HRFF	= A_CBM

VSYNC	= B_CBM

Y (7)  = DBD_DTIN  	UV (7)  = A_VREQZ

Y (6)  = DBU_DTIN	UV (6)  = B_VREQZ

Y (5)  = MWB_DTIN	UV (5)  = A_VGNTZ

Y (4)  = MRB_DTIN	UV (4)  = B_VGNTZ

Y (3)  = IPTS_DTIN	UV (3)  = CB_A_MX

Y (2)  = EPTS_DTIN	UV (2)  = CB_B_MX

Y (1)  = IPMS_DTIN	UV (1)  = R2_A_MX

Y (0)  = EPMS_DTIN	UV (0)  = R2_B_MX

## Serial Power Control Register

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| BEh | PPSPCWR | RW | - | - | SCLK | SLT | SOFL | SMOD | SCKMD | SPEN | 03h |

D7-6:	Reserved

RW enabled.

D5:	SPWRCLK

1b: 32  X  PCICLK

0b: 1     X  PCICLK

D4:	SPWRLT

1b: Half-CLOCK timing

0b: CLOCK sync timing

D3:	PWROFL

1b:Hi-z

0b:0v

D2:	PWRMOD

1b: MICREL  MIC2546 mode

0b: TI               TPS2216/14 mode

D1:	PWRCKMOD

1b: Input mode  32kHz CLOCK is input to CLOCK/CLK32 terminal.

0b: Output mode  Serial Bus Logic set in D5 is output.

D0:	SPWREN

1b: Serial Power Mode

Power control – Serial mode

ISA_IRQ parallel output is enabled.

0b: Parallel Power Mode

Power control – Parallel mode

ISA_IRQ parallel mode is disabled.

## IRQ Routing Register

| Config | NAME | RW | D31 | D30 | D29 | D28 | D27 | D26 | D25 | D24 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C0h | IRQRTG | R/W | IRQMUX7 | IRQMUX6 | 0000h 0000h |
|  |  |  | D23 | D22 | D21 | D20 | D19 | D18 | D17 | D16 |  |
|  |  |  | IRQMUX5 | IRQMUX4 |  |
|  |  |  | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 |  |
|  |  |  | IRQMUX3 | IRQMUX2 |  |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 |  |
|  |  |  | IRQMUX1 | IRQMUX0 |  |

# D31-D28:		IRQMUX7 Routing

# Assign one of the 12 interrupts (SMI,IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX7.

# D27-D24:		IRQMUX6 Routing

# Assign one of the 12 interrupts (SMI, IRQ3,4,5,7,9,10,11,12,14,15) to

# IRQMUX6.

# D23-D20:	IRQMUX5 Routing

# Assign one of the 12 interrupts (SMI, IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX5.

# D19-D16:	IRQMUX4 Routing

# Assign one of the 13 interrupts (SMI, RIOUT, IRQ3, 4,5,7,9,10,11,12,14,15) to IRQMUX4.

# D15-D12:	IRQMUX3 Routing

# Assign one of the 12 interrupts (RIOUT, IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX3.

# D11-D8:	IRQMUX2 Routing

# Assign one of the 12 interrupts (SMI, IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX2.

# D7-D4:	IRQMUX1 Routing

# Assign one of the 12 interrupts (SMI, IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX1.

# D3-D0:	IRQMUX0 Routing

# Assign one of the 13 interrupts (INTB, SMI, IRQ3, 4,5,7,9,10,11,12,14,15) to

# IRQMUX0.

| Routing bit | IRQMUX7 | IRQMUX6 | IRQMUX5 | IRQMUX4 | IRQMUX3 | IRQMUX2 | IRQMUX1 | IRQMUX0 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0000b | No IRQ Routing |
| 0001b | No IRQ Routing | RIOUT | RIOUT | No IRQ Routing | INTB |
| 0010b | SMI |
| 0011b | IRQ3 |
| 0100b | IRQ4 |
| 0101b | IRQ5 |
| 0110b | No IRQ Routing |
| 0111b | IRQ7 |
| 1000b | No IRQ Routing |
| 1001b | IRQ9 |
| 1010b | IRQ10 |
| 1011b | IRQ11 |
| 1100b | IRQ12 |
| 1101b | No IRQ Routing |
| 1110b | IRQ14 |
| 1111b | IRQ15 |

## Additional Control Register

This register is for internal signal trace.

Only one is existence in this controller.   (A, B common register)

| Config | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| C4h | NVADC | R | - | - | - | - | - | - | SACTS | PSSPS | 00h |

# D7-2:		Reserved

# 0b : fixed.

D1:		Socket Activity Status Bit

1b : Card Socket is Active.  Access from PC Card is enabled.

0b : Card Socket is not non-Active.  Access from PC Card is disabled.

D0:		Power Stream in Progress Status Bit

1b : Enable

Instruction to Card Slot Power Switch is enabled.

0b : Disable

Instruction to Card Slot Power Switch is disabled.

## Configuration Control Register

This register controls Configuration Register and interrupt.

Only one exists in this controller.

(A, B common register)

| Config | NAME | RW | D31 |  |  |  |  |  |  | D16 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| FCh | PPCNF | RW | - |  |  |  |  |  |  | - | 0000h |
|  |  |  | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
|  |  |  | IR15LE | IR14LE | IR12LE | IR11LE | IR10LE | IR9LE | IR7LE | IR6LE | 00h |
|  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
|  |  |  | IR5LE | IR4LE | IR3LE | - | SIROE | DSKST | SIRMS | IDWE | 00h |

# D31-D16:	Reserved

0b : fixed

D15:		IRQ15 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ15 at serial interrupt transmission.

0b : Edge Trigger

1b : Level Trigger

D14:		IRQ14 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ14 at serial interrupt transmission.

0b : Edge Trigger

1b : Level Trigger

D13:		IRQ12 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ12 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D12:		IRQ11 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ11 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D11:		IRQ10 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ10 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D10:		IRQ9 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 9 at serial interrupt transmission.

0b : Edge Trigger

1b : Level Trigger

D9:		IRQ7 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 7 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D8:		IRQ6 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 6 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D7:		IRQ5 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 5 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D6:		IRQ4 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 4 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D5:		IRQ3 Level/Edge Select bit

This bit selects Edge Trigger or Level Trigger of IRQ 3 at serial interrupt

transmission.

0b : Edge Trigger

1b : Level Trigger

D4:		Reserved

0b : fixed

D3:		Serial Interrupt Output Enable bit

This bit is an output enable bit of the serial interrupt signal of this

controller.

0b : The serial interrupt signal of is disabled.  However, the clock for serial

interrupt is received and keep synchronized.

1b : The output of the serial interrupt signal is enabled.  When this bit changes to

1b (Permission)    from 0b (stop), interrupts which had collected by then is

cleared.

D2:		Deskstation Type bit

0b : DeskStation9 can be connected.

1b : DeskStation8 can be connected.

D1:		Serial Interrupt Mode Select bit

This bit selects serial interrupt mode.

0b : New Serial Interrupt Mode. (New : Receive Rising Edge or Break Edge, or receive

Level)

1b : Conventional Serial Interrupt Mode. (Conventional : Receive only Rising Edge.)

D0:		ID register Write Enable bit

1b: Enable

Write is enabled for the following Configuration Register.

Vendor ID  	(Offset:00h)

Device ID 	(Offset: 02h)

Status ID 						(Offset: 06h:bit4)

Revision ID	(Offset: 08h)

Class Code						 (Offset: 09h)

Subsystem Vender ID Register				 (Offset: 40h)

Subsystem Device ID Register				 (Offset: 42h)

Power Management Capabilities Register 	(Offset: 82h:bit15, 5-3)

Power Management Control/Status Register			 (Offset: 84h:bit14-13)

PMCSR PCI to CardBus Bridge Support Extensions Register	 (Offset: 86h:bit7-6)

Data Register						 (Offset: 87h)

0b: Disable

Read only.

# PC-Card16 Register

This controller has Register Set for PC-Card16 cards.

Access to Register Sets is enabled after Slot Control Register - SLOTENbit (Config.Reg. A0h - D6) is activated. (=1) (Address decoding is started.)

Register sets are mapped by the 2 K byte space on the memory space of a system which starts

from the address which added 2 K bytes (800h) of offset to the base address hold Base

Address Register (Config.offset: 10h).

8.1	Identification and Revision Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 00h | 800 | PPRVN | RW | ID1 | ID0 | - | - | REV3 | REV2 | REV1 | REV0 | 00h |

# D7-D6:	PCMCIA Card Type ID

D3-D0:	Revision

This register does not affect PC Card.

This register can write when D4 (Slot Control Register (Config: A0h)) is set to 0.

(Ref.) The controller of EXCA compatible by Intel can read 83h when reading this

register. (B-step compliant of EXCA)  A-step compliant can read 82h.

8.2	Interface Status Register

Description in parentheses is a terminal name when selecting I/O Card Interface (Offset 03h, D5 = 1)

This register is read only, and the status of each terminal can be seen as register data.

This register does not affect performance of this controller.

Data is latched at Break Edge of IORD#, and the data is read so that the read data may not change to the change in a read cycle.

As to BVD2、Ready/Busy、Write Protect , it is fixed to HI when the card is not inserted because of the internal gate.

Reserved bit of D7 can always read H1.

Card Power Active bit of D6 can read the status of a power supply of the card. (1 at the time of power supply impression)

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 01h | 801 | PPIFS | R | - | CPA | BSY# | WP | CD2# | CD1# | BVD2 | BVD1 | - |

D7:		Reserved (1b fixed)

D6:		Card Power Active

1b : Card Power Supply (5V) provided.

0b : Card Power Supply (5V) not provided.

D5:	BSY# Status

Indicate the status of an external input signal BSYA#/BSYB#.

D4:		WP Status

Indicate the status of an external input signal WPA/WPB.

D3:		CD2# Status

Indicate the status of an external input signal CD2A#/CD2B#.

D2:		CD1# Status

Indicate the status of an external input signal CD1A#/CD1B#.

D1:		BVD2 Status

Indicate the status of an external input signalBVD2A/BVD2B.

D0:		BVD1 Status

Indicate the status of an external input signal BVD1A/BVD1B.

Indicate 1 when BSY#, WP and BVD2 Card are not inserted.

8.3	Power Control Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 02h | 802 | PPPCN | RW | COE | DRCL | EAPS | CP5E | CP3E | - | VPP1 | VPP0 | 00h |

# D7:		Output Enable

# Enable/Disable of I/F signal for the following cards.

# CE1#, CE2#, OE#, WE#/PGM#, IORD#, IOWR#, REG#, RESET, A25-00,

# D15-00

# 1b:  Enable

# 0b:  Disable (Hi-z)

D6:	Disable Resume Reset

0b: Enable

CARD 16 Reg. is initiated by Resume Reset.

1b: Disable

CARD 16 Reg. maintain the value when Resume Reset.

All the registers of PC-Card16 are the subject to reset to

SUPEND/RESUME.

D5:		Auto Power Switch enable

0b: Enable

Card Power Supply enabled with/without the card is put in.

1b: Disable

Card Power Supply disabled without the card is put in.

D4:		Card Power Enable (1)

0b:  Card Power Supply disabled.

1b:  Card Power Supply enabled.

However, when this bit is “1” but D5 is “1” AND the card is not inserted in the slot, power supply to the slot is disabled.

D3:		Card Power Enable (0)

This bit is invalid when ToPIC100 Function Control Register (Card16.3Eh) bit 0 (Power Control Enable) is 0.

RW possible register.

When The ToPIC100 Function Control Register (3Eh) bit 0 (Power Control Enable) is 1 AND D4 is 1, Power Control Terminal will change to output the voltage as follows.

1b: 3v

0b: 5v

However, when D4 is 1, D5 is 1 AND the card is not inserted in the slot, Power Supply is disabled.

| Card Power Enable | Power Control Register |  |
| --- | --- | --- |
| 3Eh D0 | D4 | D3 | Power Supply Mode |
| 0 | 0 | - | 0 v |
| 0 | 1 | - | 5 v |
| 1 | 0 | - | 0 v |
| 1 | 1 | 0 | 5 v |
| 1 | 1 | 1 | 3 v |

*D4, 3 compatible with 82092AA.

# D2:		Reserved

# RW possible.  No affect to this controller.

D1-D0:	VPP Control Bit1-0

Slot Power Supply (VPP) controlled.

| D1 | D0 | VPP Power Supply Mode |
| --- | --- | --- |
| 0 | 0 | 0.0 v |
| 0 | 1 | VCC |
| 1 | 0 | 12 v |
| 1 | 1 | Reserved |

# D4, D1, D0 and Card Power Supply

# Card Power Supply signal changes its output signal as follows with the setting of PWRSIGS1 signal.

ToPIC100 Function Control Register (Card16. 3Eh) D0=0

| CARD ON* | Power Control Register (Offset:02h) | Power Supply Provided |
| --- | --- | --- |
|  | D5 | D4 | D3 | D1 | D0 | VCC | VPP |
| X | X | 0 | X | X | X | 0 | 0 |
| X | 0 | 1 | X | 0 | 0 | 5 | 0 |
|  |  |  |  | 0 | 1 |  | 5 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
| 1 | 1 | 1 | X | 0 | 0 | 5 | 0 |
|  |  |  |  | 0 | 1 |  | 5 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
| 0 | 1 | 1 | X | X | X | 0 | 0 |

# ToPIC100 Function Control Register (3Eh) D0=1

| CARD ON* | Power Control Register (Offset:02h) | Power Supply Provided |
| --- | --- | --- |
|  | D5 | D4 | D3 | D1 | D0 | VCC | VPP |
| X | X | 0 | X | X | X | 0 | 0 |
| X | 0 | 1 | 0 | 0 | 0 | 5 | 0 |
|  |  |  |  | 0 | 1 |  | 5 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
| X | 0 | 1 | 1 | 0 | 0 | 3.3 | 0 |
|  |  |  |  | 0 | 1 |  | 3.3 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
| 1 | 1 | 1 | 0 | 0 | 0 | 5 | 0 |
|  |  |  |  | 0 | 1 |  | 5 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
|  | 1 | 1 | 1 | 0 | 0 | 3.3 | 0 |
|  |  |  |  | 0 | 1 |  | 3.3 |
|  |  |  |  | 1 | 0 |  | 12 |
|  |  |  |  | 1 | 1 |  | 0 |
| 0 | 1 | 1 | X | X | X | 0 | 0 |

*CARD ON indicates the status which that Card put in when set to 1.

8.4	Interrupt and General Control Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 03h | 803 | PPICN | RW | ERI | CRST | CTYP | ESMI | PIR3 | PIR2 | PIR1 | PIR0 | 00h |

# D7:		Ring Indicate Enable

# 1b: Enable

# STSCHG signal output from PIN “RIOUT” (I/O Card Mode)

# 0b: Disable

# Always read “0” in CARD16 Reg. 04h-D0.

D6:		Card Reset

Reversal of 0b/1b set in this bit is output from CRESET terminal.

CRESET signal is activated when setting 0. (Soft Reset)

D5:		Card Type

1b:  I/O Card Mode

0b:  Memory Card Mode

D4:		SMI Enable

1b: Assign ”SMI” (output from PIN“IRQDTZ” at SMI timing of serial INT)

0b: Assign “IRQX” (output from PIN”IRQDTZ” at IRQX timing of serial INT)

D3-D0:	I/O IRQ Bit 3-0)

This bit is for mapping the input from IREQ terminal at I/O Card IF Mode

to IRQ of the system.  In the following table, when setting to Reserved,

same performance as IRQ Not Selected.

| D3 | D2 | D1 | D0 | IRQ LEVEL |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | IRQ Not Selected |
| 0 | 0 | 0 | 1 | Reserved |
| 0 | 0 | 1 | 0 | Reserved |
| 0 | 0 | 1 | 1 | IRQ3 Enable |
| 0 | 1 | 0 | 0 | IRQ4 Enable |
| 0 | 1 | 0 | 1 | IRQ5 Enable |
| 0 | 1 | 1 | 0 | Reserved |
| 0 | 1 | 1 | 1 | IRQ7 Enable |
| 1 | 0 | 0 | 0 | Reserved |
| 1 | 0 | 0 | 1 | IRQ9 Enable |
| 1 | 0 | 1 | 0 | IRQ10 Enable |
| 1 | 0 | 1 | 1 | IRQ11 Enable |
| 1 | 1 | 0 | 0 | IRQ12 Enable |
| 1 | 1 | 0 | 1 | Reserved |
| 1 | 1 | 1 | 0 | IRQ14 Enable |
| 1 | 1 | 1 | 1 | IRQ15 Enable |

  - Card Status Change Register

This register is read only, and holds the status of change for Card Status Signal.  However, write operation may have an affection. (Refer to the following register clear method)

When Card Status Signal set as enabled by Card Status Change Control Register (Card16. 05h) has changes, “1” is set to the bit related to this register.  And interrupt occurs from IRQ line simultaneously, which selected by CSC IRQ Bit 3-0. ( or SMI occurs)

A disabled bit set by Card Status Change Control Register (Card16. 05h) has no “1” even if the related status signal has a change.

Two methods in clearing the “1” bit in this register.  If D2=0 (Global Control Register (Card16. 1Eh)), D3 – D0 having “1” will be cleared and IRQ line (or SMI) becomes inactive only by reading this register.

When D2=1 (Global Control Register), it’s not cleared by reading. It can be cleared by writing “1” to the bit. (Write Back Mode)  Since every 1 bit can be cleared, all bits have to be cleared to inactivate IRQ line (or SMI).

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 04h | 804 | PPCSC | R | - | - | - | - | CDC | RDYC | BATW | BATD | 00h |

# D3:		Card Detect Change

# 1: Changed

# 0: Not changed

Set up when CD1 terminal and CD2 terminal are changed from “LL” to

“LH” or “HL” (Detected the Card pulled out) , or are changed  from

“HH” to “LL” (Detected the Card is put in).  But cannot be sensed as to

Detect during suspended.  This bit can set the status same with the

Card  (Software Card Detect) actually inserted or removed by writing

“1” to D5 (Soft Wear Card Detect Interrupt) of Additional General

Control Register (Offset 16h).  It is effective only when D3 of Card

Status Change Control Register (Offset 05h) is “1”,  and it does not

change when D3 is “0”.   Software Card Detect is also invalid.

D2:		Ready Change)

1: Changed

Card status Change Interrupt will occur due to RDY/#BSY signal

switched to “H” form “L” in case of Memory Card IF.  Set up once, or

never be 0 even if returned to “L”.

0: Not changed

In either case of Memory Card whose status is not changed or I/O Card.

D1:		Battery Warning

1: Battery Warning

Set up in case of Memory Card Battery Warning (an external input

signal BVD1A/BVD1B and BVD2A/BVD2B are changed from “HH”

from “HL”).  Set up once, or never be 0 even if returned to Battery

Good (“HH”).  When BVD1A is changed to “L” (Battery Dead), this bit

will be cleared.

0: Not Battery Warning

In either case of Battery Warning whose status is not changed or I/O

Card.

D0:		Battery Dead

1: Battery Dead

Set up in case of Memory Card, and when Battery Good status or  Battery Warning

switched to Battery Dead status (an external input signal BVD1A/BVD1B is

changed to “L”, and Card Status Change Interrupt will occur.  Set up once, or

never be 0 even if returned to Battery Good (“H”) or Battery Warning.

0: Not Battery Dead

In either case of Battery Dead whose status is not changed or I/O Card.

Bit is reset by following way in this Register (=0).

This register reads when D2 (Global Control Register (Offset: 1Eh)) is set to 0.

1 will be written to each bit when D2 (Global Control Register) is set to 1.

After Card- Put in, D2-D0 will not be sensed between 1ms.

8.6	Card Status Change Interrupt Control Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 05h | 805 | PPCSI | RW | CIR3 | CIR2 | CIR1 | CIR0 | ECDD | ERCH | EBAW | EBAD | 00h |

# D7-D4:	CSC IRQ Bit 3-0

Assigns the interrupt by Card Status Change to PIC interrupt input.

D3:		Card Detect Enable

1b: Enable

Interrupt by Card Detect Change enabled.

0b: Disable

interrupt by Card Detect Change disabled.

D2:		Ready Enable

1b: Enable

Interrupt by READY Change enabled.

0b: Disable

Interrupt by READY Change disabled.

Ready Change Detect is always disabled in case of I/O Card IF.

D1:		Battery Warning Enable

1b: Enable

Interrupt by BATTERY WARNING enabled.

0b: Disable

Interrupt by BATTERY WARNING disabled.

In case of interrupt by BATTERY WARNING enabled, CSC INT (or SMI) will

occur when BVD2 signal is changed to “L” from “H”.

BATTERY WARNING Detect is always disabled in case of I/O Card IF.

D0:		Battery Dead Enable / (STSCHG# Enable)

1: Enable

Interrupt by BATTERY DEAD enabled.

0: Disable

Interrupt by BATTERY DEAD disabled.

In case of interrupt by BATTERY DEAD enabled, CSC INT (or SMI) will

occur when 	BVD1 signal is changed to “L” from “H”.

BATTERY DEAD Detect is always disabled in case of I/O Card IF.

D7-D4 (CSC IRQ Bit3-0)  and IRQ**

| D7 | D6 | D5 | D4 | IRQ LEVEL |
| --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | IRQ Not Selected |
| 0 | 0 | 0 | 1 | Reserved |
| 0 | 0 | 1 | 0 | Reserved |
| 0 | 0 | 1 | 1 | IRQ3 Enable |
| 0 | 1 | 0 | 0 | IRQ4 Enable |
| 0 | 1 | 0 | 1 | IRQ5 Enable |
| 0 | 1 | 1 | 0 | Reserved |
| 0 | 1 | 1 | 1 | IRQ7 Enable |
| 1 | 0 | 0 | 0 | Reserved |
| 1 | 0 | 0 | 1 | IRQ9 Enable |
| 1 | 0 | 1 | 0 | IRQ10 Enable |
| 1 | 0 | 1 | 1 | IRQ11 Enable |
| 1 | 1 | 0 | 0 | IRQ12 Enable |
| 1 | 1 | 0 | 1 | Reserved |
| 1 | 1 | 1 | 0 | IRQ14 Enable |
| 1 | 1 | 1 | 1 | IRQ15 Enable |

8.7	Window Enable Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 06h | 806 | PPWEN | RW | IOW1 | IOW0 | - | MEW4 | MEW3 | MEW2 | MEW1 | MEW0 | 00h |

# D7:		I/O Window 1 Enable

# 1b: Card I/O WINDOW 1 Enable

# I/O Access within the address limit specified by Offset 0Ch-Offset 0Fh

# is I/O  Access to the Card.  CPU address is output directly for A15-00

# and ALL0 for A25-16.

# 0b: Card I/O WINDOW 1 Disable

# I/O access cycle does not occur even if I/O access from within the

# address limit specified by Offset 0Ch-Offset 0Fh.

D6:		I/O Window 0 Enable

1b: Card I/O WINDOW 0 Enable

I/O Access within the address limit specified by Offset 08h-Offset 0Bh

is I/O  Access to the Card.  CPU address is output directly for A15-00

and ALL0 for A25-16.

0b: Card I/O WINDOW 0 Disable

I/O Access cycle does not occur even if I/O Access from within the

address limit specified by Offset 08h-Offset 0Bh.

D4:		Memory Window 4 Enable

1b: Card  MEMORY WINDOW 4 Enable

Memory Access within the address limit specified by Offset 30h-Offset

33h will be Memory Access to the Card.  In this case, CPU address is

output directly for A11-00,  and A25-12 will be added the value of

Offset specified by the Register (34h, 35h).

0b: Card MEMORY WINDOW 4 Disable

Memory Access Cycle does not occur even if Memory Access is from

within the  address limit specified by Offset 30h-Offset 33h.

D3:	Memory Window 3 Enable

1b: Card  MEMORY WINDOW 3 Enable

Memory Access within the address limit specified by Offset 28h-Offset

2Bh will be Memory Access to the Card.  In this case, CPU address is

output directly for A11-00,  and A25-12 will be added the value of

Offset specified by the Register. (2Ch, 2Dh)

0b: Card MEMORY WINDOW 3 Disable

Memory Access does not occur even if Memory Access is from within

the address limit  specified by Offset 28h-Offset 2Bh.

D2:	Memory Window 2 Enable

1b: Card MEMORY WINDOW 2 Enable

Memory Access within the address limit specified by Offset 20h-Offset

23h will be Memory Access to the Card.  In this case, CPU address is

output directly for A11-00,  and A25-12 will be added the value of

Offset specified by the Register. (24h, 25h)

0b: Card MEMORY WINDOW 2 Disable

Memory Access Cycle does not occur even if Memory Access is from

within the  address limit specified by Offset 20h-Offset 23h.

D1:		Memory Window 1 Enable

1b: Card MEMORY WINDOW 1 Enable

Memory Access within the address limit specified by Offset 18h-Offset

1Bh will be  Memory Access to the Card.  In this case, CPU address is

output directly for A11-00,

and A25-12 will be added the value of Offset specified by the Register.

(1Ch, 1Dh)

0b: Card MEMORY WINDOW 1 Disable

Memory Access Cycle does not occur even if Memory Access is from

within the  address limit specified by Offset 18h-Offset 1Bh.

D0:		Memory Window 0 Enable

1b: Card MEMORY WINDOW 0 Enable

Memory Access within the address limit specified by Offset 10h-Offset

13h will be Memory Access to the Card.  In this case, CPU address is

output directly for A11-00,  and A25-12 will be added the value of

Offset specified by the Register. (14h, 15h)

0b: Card MEMORY WINDOW 0 Disable

Memory Access Cycle does not occur even if Memory Access is from

within the  address limit specified by Offset 10h-Offset 13h.

  - I/O Window Control Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 07h | 807 | PPWCN | RW | I116 | I1ZW | I1SR | I1DS | IO16 | I0ZW | IOSR | IODS | 00h |

# D7:		I/O Window 1 Wait State

Sets up the Number of 16bit I/O Access cycle in I/O Window 1.

1b: 4 ISA CLOCK (1WAIT) MODE

0b: STANDARD BUS CYCLE (3 ISA CLOCK)

While WAIT signal from the Card is active, the Wait Cycle is inserted further and

Bus Cycle is extended. (WAIT form the Card is prioritized.)

D6:		I/O Window 1 Zero Wait State

Sets up the Number of 8bit I/O Access Cycle in I/O Window 1.

1b: 4 ISA CLOCK (0 WAIT) MODE

0b: STANDARD BUS CYCLE (6 ISA CLOCK)

When WAIT signal from the Card is active (L), 0 Wait Cycle does not occur. (WAIT

form the Card is prioritized)

D5:		I/O Window 1 –IOIS16 Source

Sets up the Data Length of I/O Access in I/O Window 1.

1b: External Input Signal “IOIS16#”.

0b: Internal Output Signal PCM_I16Z (16bit I/O) enabled (=0) when D4 is set to 1.

D4:		I/O Window 1 Data Size

Set up the I/O Access Length in I/O Window 1 when D5=0.

1b: 16bit Access (Enabled when I1SR is set to 0)

0b: 8bit Access

D3:		I/O Window 0 Wait State

Set up 16bit I/O Access Cycle Number in I/O Window 0.

1b: 4 ISA CLOCK (1WAIT) MODE

0b: STANDARD BUS CYCLE (3 ISA CLOCK)

While WAIT signal from the Card is active, the Wait Cycle is inserted further and

Bus Cycle is extended. (c.)

D2:		I/O Window 0 Zero Wait State

Sets up 8bit I/O Access Cycle Number in I/O Window 0.

1b: 4 ISA CLOCK (0 WAIT) MODE

0b: STANDARD BUS CYCLE (6 ISA CLOCK)

When WAIT signal from the Card is active (LOW), 0 Wait Cycle does not occur.

(WAIT from the  Card is prioritized.)

D1:		I/O Window 0 –IOIS16 Source

Sets up the Data Length of I/O Access in I/O Window 0.

1b: External Input Signal “IOIS16#”.

0b: Register Sets up (D4)

D0:		I/O Window 0 Data Size

Set up the I/O Access Length in I/O Window 0 when D5=0.

1b: 16bit Access

0b: 8bit Access

Disabled when D5=1.

8.9	I/O Window 0 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 08h | 808 | PPI0S | RW | I0S7 | I0S6 | I0S5 | I0S4 | I0S3 | I0S2 | I0S1 | I0S0 | 00h |

# D7-D0:	Address 7-0

Set up the start lower 8bit, which has I/O access to the Card in I/O Window 0.

8.10	I/O Window 0 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 09h | 809 | PPI0S | RW | I0SF | I0SE | I0SD | I0SC | I0SB | I0SA | I0S9 | I0S8 | 00h |

# D7-D0:	Address 8-15

Set up the start upper 8bit, which has I/O access to the Card in I/O Window 0.

8.11	I/O Window 0 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Ah | 80A | PPI0E | RW | I0E7 | I0E6 | I0E5 | I0E4 | I0E3 | I0E2 | I0E1 | I0E0 | 00h |

# D7-D0:	I/O Window 0 Stop Address 7-0

Set up Stop Address lower 8bit, which has I/O access to the Card in I/O Window 0.

8.12	I/O Window 0 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Bh | 80B | PPI0E | RW | I0EF | I0EE | I0ED | I0EC | I0EB | I0EA | I0E9 | I0E8 | 00h |

# D7-D0:	I/O Window 0 Stop Address 15-8

Set up the Stop Address upper 8bit, which has I/O access to the Card in I/O

Window 0.

8.13	I/O Window 1 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Ch | 80C | PPI1S | RW | I1S7 | I1S6 | I1S5 | I1S4 | I1S3 | I1S2 | I1S1 | I1S0 | 00h |

# D7-D0:	Address 7-0

Set up the start lower address 8bit, which has I/O access to the Card in I/O

Window 1.

8.14	I/O Window 1 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Dh | 80D | PPI1S | RW | I1SF | I1SE | I1SD | I1SC | I1SB | I1SA | I1S9 | I1S8 | 00h |

# D7-D0:	Address 8-15

# Set up the start address upper 8bit, which has I/O access to the Card in

# I/O Window 1.

8.15	I/O Window 1 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Eh | 80E | PPI1E | RW | I1E7 | I1E6 | I1E5 | I1E4 | I1E3 | I1E2 | I1E1 | I1E0 | 00h |

# D7-D0:	Address 7-0

Set up the stop address lower 8bit, which has I/O access to the Card in I/O

Window 1.

8.16	I/O Window 1 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 0Fh | 80F | PPI1E | RW | I1EF | I1EE | I1ED | I1EC | I1EB | I1EA | I1E9 | I1E8 | 00h |

# D7-D0:	Address 8-15

Set up the stop address upper 8bit, which has I/O access to the Card in I/O

Window 1.

8.17	Memory  Window 0 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 10h | 810 | PPM0S | RW | MS19 | MS18 | MS17 | MS16 | MS15 | MS14 | MS13 | MS12 | 00h |

# D7-D0:	Address 12-19

Set up the start address lower 8bit, which has memory access to the Card in System Memory Window 0.

  - Memory Window 0 Start High Address Register

This Register sets up the start address upper 4bit in Memory Window 0, and assigns data size of Memory Window and Wait control.

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 11h | 811 | PPM0S | RW | M0DS | M0ZW | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7:		Data Size

# 1b: 16bit access

# 0b: 8bit access

# D6:		Zero_WS

Set up the Number of Memory Access cycle.

|  | D6=0 | D6=1 |
| --- | --- | --- |
| 8bit MEMORY ACCESS | Standard Cycle ( 6 SYS CLK ) | 0 WAIT Cycle ( 4 SYS CLK ) |
| 16bit MEMORY ACCESS | CARD16 REG. 13H- D7, D6 | 0 WAITCycle ( 2 SYS CLK ) |

When WAIT signal is input from the Card, 0 Wait cycle does not occur even if this

bit is set to 1.  (WAIT signal from the Card is priority)

# D5-D4:	Scratch Bit

Given value can be set.  No affect to this controller.  R/W is possible.

Scratch Bit is given name by the Spec of Exca by Intel.

D3-D0:	Address 20-23

Set up the start address upper 4bit, which has memory access to the Card in

System Memory Window 0.

8.19  	Memory Window 0 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12h | 812 | PPM0E | RW | ME19 | ME18 | ME17 | ME16 | ME15 | ME14 | ME13 | ME12 | 00h |

# D7-D0:	Address 12-19

Set up the stop address lower 8bit, which has memory access to the Card in

System Memory  Window 0.

8.20	Memory Window 0 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 13h | 813 | PPM0E | RW | W0S1 | W0S0 | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7-D6:	Wait State Bit 1-0 / Memory Timing Select 2-1

Set up the cycle number of 16bit Memory Access.

0 0b:  3ISA Clock

0 1b:  4ISA Clock (1 Wait)

1 0b:  5ISA Clock (2 Wait)

1 1b:  6ISA Clock (3 Wait)

D5-D4:	Reserved

RW possible.

D3-D0:	Memory Window 0Stop Address 23-20

Set up the stop address upper 4bit, which has memory access to the Card in System

Memory  Window 0.

8.21	Memory Window 0 Offset Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 14h | 814 | PPM0O | RW | MO19 | MO18 | MO17 | MO16 | MO15 | MO14 | MO13 | MO12 | 00h |

# D7-D0:	Address 12-19

Set up the offset address lower 8bit, which has memory access to the Card in

System Memory  Window 0.

  - Memory Window 0 Offset High Address Register

Set up offset address lower 8bit of Memory Window 0.

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 15h | 815 | PPM0O | RW | E0WP | E0RG | MO25 | MO24 | MO23 | MO22 | MO21 | MO20 | 00h |

# D7:		Write Protected

1b:  Disable

0b:  Enable

Memory write enabled.  This bit is not affected by memory card.

D6:		-REG Active

1b:  Enable

REG#=0.  Access via System Memory Window will result in attribute

memory.

0b:  Disable

REG#=1.  Access via System Memory Window will result in common

memory.

D5-D0:	Address 20-25

Set up the offset address upper 6bit, which has memory access to the Card in

System Memory  Window 0.

8.23	Additional General Control Register

This Register is added by ExCAB-STEP by Intel.

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 16h | 816 | PPACN | RW | VS2 | VS1 | SWD | - | - | - | CRR | - | 00h |

# D7:		Voltage Sense2 Status

Indicate the status of an external input signal VS2A/VS2B when D1 (Function

Register Offset : 3Eh) is set to 1b.

D6:		Voltage Sense1 Status

Indicate the status of an external input signal VS1A/VS1B when D1 (Function

Register Offset : 3Eh) is set to 1b.

D5:		(S/W Card Detect Interrupt) - Read Zero

Writing “1” to this bit when Card Status Change Interrupt Control Register –

Card Detect Enable (CARD16 REG. 05H-D3) = 1 (Detection of the Card inserted /

removed is permitted) occurs Card Status Change Interrupt while sets up 1 in D3

(Card Detect Change) of Card Status Change Register, Offset 04h.

It is called Software Card Detect function that makes to look like there have been inserted / removed of the Card by the Software.

Software Card Detect Interrupt by this bit is completely equivalent to Card Detect Change Interrupt by insert / removal of the Card in hardware-wise.

This function is invalid when D3 (Offset 05h, Card Status Change Interrupt Control Register) is set to 0.

The Register bit does not exist in hardware-wise, and always can 0b when read even

if 1 is written.

# D4-D2:	Reserved

# R/W possible.

D1:		Card Removal Reset

1b: Register Reset

When the R2 Card is removed, all the CARD16 Registers except for the following Register are reset.

0b: No Register Reset

Registers not reset

Offset 00h (Identification and Revision Register) all bits

Offset 01h (Interface Status Register) all bits

Offset 02h (Power Control Register) all bits

Offset 03h (Interrupt and General Control Register) D4

Offset 04h (Card Status Change Register) all bits

Offset 05h (Card Status Change Interrupt Control Register) all bits

Offset 16h (Additional Control Register) all bits

Offset 1Eh (Global Control Register) all bits

Offset 3Bh (ToPIC100 Card Timing Register) all bits

Offset 3Ch (Audio / Video Switching Register) all bits

Offset 3Eh (ToPIC100 Function Control Register) all bits

Offset 3Fh (Toshiba Hidden Register) all bits

# D0:		Reserved

R/W possible.

8.24	Memory Window 1 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 18h | 818 | PPM1S | RW | MS19 | MS18 | MS17 | MS16 | MS15 | MS14 | MS13 | MS12 | 00h |

# D7-D0:	Memory Window 1 Start Address 19-12

Set up the start address lower 8bit, which has memory access to the Card in

Memory Window 1.

8.25	Memory Window 1 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 19h | 819 | PPM1S | RW | M1DS | M1ZW | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7:		Data Size

Set up the Data length when memory access to MEMORY WINDOW 1.

1b: 16bit Access

0b:  8bit Access

D6:		Zero_WS

|  | D6=0 | D6=1 |
| --- | --- | --- |
| 8bit MEMORY ACCESS | Standard Cycle ( 6 SYS CL) | 0 WAIT Cycle ( 4 SYS CLK) |
| 16bit MEMORY ACCESS | Set up by CARD16 REG. 1BH- D7, D6 | 0 WAIT Cycle (2 SYS CLK) |

When WAIT signal is input from the Card, 0 WAIT Cycle does not occur even if	D6=1. (WAIT signal from the Card is prioritized.)

# D5-D4:	Reserved

# R/W possible.

D3-D0:	Address 20-23

Set up the start address upper 4bit, which has memory access to the Card in

Memory Window 1.

8.26	Memory Window 1 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Ah | 81A | PPM1E | RW | ME19 | ME18 | ME17 | ME16 | ME15 | ME14 | ME13 | ME12 | 00h |

# D7-D0:	Memory Window 1 Stop Address 19-12

Set up the stop address lower 8bit, which has memory access to the Card in

Memory Window 1.

8.27	Memory Window 1 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Bh | 81B | PPM1E | RW | W1S1 | W1S0 | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7-D6:	Memory Window 1 16bit Memory Access Length

Set up Cycle Number of 16bit Memory Access

0 0b: 3 ISA Clock

0 1b: 4 ISA Clock (1 Wait)

1 0b: 5 ISA Clock (2 Wait)

1 1b: 6 ISA Clock (3 Wait)

D5-D4:	Reserved

R/W possible.

D3-D0:	Memory Window 1 Stop Address 23-20

Set up the stop address upper 4bit, which has memory access to the Card in

Memory Window.

8.28	Memory Window 1 Offset Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Ch | 81C | PPM1O | RW | MO19 | MO18 | MO17 | MO16 | MO15 | MO14 | MO13 | MO12 | 00h |

# D7-D0:	Memory Window 1 Offset Address 19-12

Set up the Offset Address lower 8bit, which has memory access to the Card in

Memory Window 1.

8.29	Memory Window 1 Offset High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Dh | 81D | PPM1O | RW | E1WP | E1RG | MO25 | MO24 | MO23 | MO22 | MO21 | MO20 | 00h |

# D7:		Write Protect

1b: Disable

0b: Enable

Memory write enabled. This bit is not affected by memory card.

D6:		-REG Active

1b: REG#=0  Attribute memory of the Card will be accessible.

0b: REG#=1  Common memory of the Card will be accessible.

D5-D0:	Address 20-25

Set up the Offset address upper 6 bit, which has memory access to the Card in

Memory Window 1.

8.30		Global Control Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1Eh | 81E | PPGCN | RW | - | - | - | - | - | RCSC | - | - | 00h |

# D7-D3:	Reserved

# R/W possible.

D2:		Card Status Change Register Initialization

1b: Initialize by Write Back

This bit is reset by writing 1 to D1 [Card Status Change Register (Offset:

04H)] (Possible  to reset separate bit)

0b: Initialize by Read

All bits (Card Status Change Register) are reset (=0) when CARD16 REG.

04H is read, and interrupt by Card Status Change Register is canceled.

(Impossible to reset separate bit.)

This Register is common to Slot A and Slot B.  If accessed from either, accessed to

the same Register.

8.31	Memory Window 2 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 20h | 820 | PPM2S | RW | MS19 | MS18 | MS17 | MS16 | MS15 | MS14 | MS13 | MS12 | 00h |

# D7-D0:	Memory Window 2 Start Address 19-12

Set up the start address lower 8bit, which has memory access to the Card in

Memory Window 2.

8.32	Memory Window 2 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 21h | 821 | PPM2S | RW | M2DS | M2ZW | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7:		Data Size

Set up data length of memory access to MEMORY WINDOW 2.

1b: 16bit access

0b:  8bit access

D6:		Zero_WS

|  | D6=0 | D6=1 |
| --- | --- | --- |
| 8bit MEMORY ACCESS | Standard cycle ( 6 SYS CLK) | 0 WAIT cycle (4 SYS CLK) |
| 16bit MEMORY ACCESS | Set up by CARD16 REG. 23H- D7, D6 | 0 WAIT cycle ( 2 SYS CLK) |

When WAIT signal is input from the Card, 0 WAIT cycle does not occur even if

D6=1. (WAIT signal from the Card is prioritized.)

# D5-D4:	Reserved

# R/W possible.

D3-D0:	Address 20-23

Set up the start address upper 4bit, which has memory access to the Card in

Memory Window 2.

8.33		Memory Window 2 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 22h | 822 | PPM2E | RW | ME19 | ME18 | ME17 | ME16 | ME15 | ME14 | ME13 | ME12 | 00h |

# D7-D0:	Memory Window 2 Stop Address 19-12

Set up the stop address lower 8bit, which has memory access to the Card in

Memory Window 2.

8.34		Memory Window 2 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 23h | 823 | PPM2E | RW | W2S1 | W2S0 | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7-D6:	Memory Window 2 16bit Memory Access Length

Set up the cycle number of 16bit Memory Access.

0 0b: 3 ISA Clock

0 1b: 4 ISA Clock (1 Wait)

1 0b: 5 ISA Clock (2 Wait)

1 1b: 6 ISA Clock (3 Wait)

D5-D4:	Reserved

R/W possible.

D3-D0:	Memory Window 2 Stop Address 23-20

Set up the stop address upper 4bit, which has memory access to the Card in

Memory Window 2.

8.35		Memory Window 2 Offset Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 24h | 824 | PPM2O | RW | MO19 | MO18 | MO17 | MO16 | MO15 | MO14 | MO13 | MO12 | 00h |

# D7-D0:	Memory Window 2 Offset Address 19-12

Set up the Offset address lower 8bit which is added to the address, which has

memory access to the Card in Memory Window.

8.36	Memory Window 2 Offset High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 25h | 825 | PPM2O | RW | E2WP | E2RG | MO25 | MO24 | MO23 | MO22 | MO21 | MO20 | 00h |

# D7:		Write Protect

# 1b:  Disable

# 0b:  Enable

# Memory Write enabled.  This bit is not affected by memory

# read.

# D6:		-REG Active

1b: REG#=0  Attribute memory of the Card will be accessible.

0b: REG#=1  Common memory of the Card will be accessible.

D5-D0:	Address 20-25

Set up the Offset address upper 6bit, which has memory access to the Card in

Memory Window 0.

8.37	Memory Window 3 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 28h | 828 | PPM3S | RW | MS19 | MS18 | MS17 | MS16 | MS15 | MS14 | MS13 | MS12 | 00h |

# D7-D0:	Memory Window 3 Start Address 19-12

Set up the start address lower 8bit, which has memory access to the Card in

Memory Window 3.

8.38	Memory Window 3 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 29h | 829 | PPM3S | RW | M3DS | M3ZW | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7:		Data Size

# 1b :  16bit access

# 0b :   8bit access

D6:		Zero_WS

|  | D6=0 | D6=1 |
| --- | --- | --- |
| 8bit MEMORY ACCESS | Standard cycle ( 6 SYS CLK) | 0 WAIT Cycle (4 SYS CLK) |
| 16bit MEMORY ACCESS | Set up by CARD16 REG. 2BH- D7, D6 | 0 WAIT Cycle (2 SYS CLK) |

When WAIT signal is input from the Card, 0 WAIT cycle does not occur even if

D6=1. (WAIT signal  from the Card is prioritized.)

# D5-D4:	Reserved

# R/W possible.

D3-D0:	Address 20-23

Set up the start address upper 4bit, which has memory access to the

Card in Memory Window 3.

8.39	Memory Window 3 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Ah | 82A | PPM3E | RW | ME19 | ME18 | ME17 | ME16 | ME15 | ME14 | ME13 | ME12 | 00h |

# D7-D0:	Memory Window 3 Stop Address 19-12

Set up the stop address lower 8bit, which has memory access to the Card in

Memory Window 3.

8.40	Memory Window 3 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Bh | 82B | PPM3E | RW | W3S1 | W3S0 | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7-D6:	Memory Window 3 16bit Memory Access Length

Set up the Cycle Number of 16bit Memory Access

00b:  3 ISA Clock

01b:  4 ISA Clock (1 Wait)

10b:  5 ISA Clock (2 Wait)

11b:  6 ISA Clock (3 Wait)

D5-D4:	Reserved

R/W possible.

D3-D0:	Memory Window 3 Stop Address 23-20

Set up the stop address upper 4bit, which has memory access to the Card in

Memory Window 3.

8.41	Memory Window 3 Offset Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Ch | 82C | PPM3O | RW | MO19 | MO18 | MO17 | MO16 | MO15 | MO14 | MO13 | MO12 | 00h |

# D7-D0:	Memory Window 3 Offset Address 19-12

Set up the Offset address lower 8bit which is added to the address, which has

memory access to the

Card in Memory Window 3.

8.42	Memory Window 3 Offset High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2Dh | 82D | PPM3O | RW | E3WP | E3RG | MO25 | MO24 | MO23 | MO22 | MO21 | MO20 | 00h |

# D7:		Write Protect

# 1b:  Disable

# 0b:  Enable

# Memory write enabled.

# This bit is not affected by memory read.

D6:		-REG Active

1b: REG#=0  Attribute memory of the Card will be accessible.

0b: REG#=1  Common memory of the Card will be accessible.

D5-D0:	Address 20-25

Set up the Offset address upper 6bit, which has memory access to the Card in

Memory Window 0.

8.43	Memory Window 4 Start Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 30h | 830 | PPM4S | RW | MS19 | MS18 | MS17 | MS16 | MS15 | MS14 | MS13 | MS12 | 00h |

# D7-D0b:	Memory Window 4 Start Address 19-12

Set up the start address lower 8bit, which has memory access to the Card in

Memory Window 4.

8.44	Memory Window 4 Start High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 31h | 831 | PPM4S | RW | M4DS | M4ZW | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7:		Data Size

# 1b :  16bit Access

# 0b :   8bit Access

D6:		Zero_WS

|  | D6=0 | D6=1 |
| --- | --- | --- |
| 8bit MEMORY ACCESS | Standard Cycle (6 SYS CLK) | 0 WAIT Cycle (4 SYS CLK) |
| 16bit MEMORY ACCESS | Set up by CARD16 REG. 33H- D7, D6 | 0 WAITCycle ( 2 SYS CLK) |

When WAIT signal is input from the Card, 0 WAIT cycle does not occur even if

D6=1. (WAIT signal  from the Card is prioritized.)

# D5-D4:	Reserved

# R/W possible.

D3-D0:	Address 20-23

Set up the start address upper 4bit, which has memory access to the Card in

Memory Window 4.

8.45	Memory Window 4 Stop Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 32h | 832 | PPM4E | RW | ME19 | ME18 | ME17 | ME16 | ME15 | ME14 | ME13 | ME12 | 00h |

# D7-D0:	Memory Window 4 Stop Address 19-12

Set up the stop address lower 8bit, which has memory access to the Card in

Memory Window 4.

8.46	Memory Window 4 Stop High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 33h | 833 | PPM4E | RW | W4S1 | W4S0 | - | - | MS23 | MS22 | MS21 | MS20 | 00h |

# D7-D6:	Memory Window 4 16bit Memory Access Length

# Set up the cycle number of 16bit Memory Access

# 0 0b: 3ISA Clock

# 0 1b: 4ISA Clock (1 Wait)

# 1 0b: 5ISA Clock (2 Wait)

# 1 1b: 6ISA Clock (3 Wait)

D5-D4:	Reserved

R/W possible

D3-D0:	Memory Window 4 Stop Address 23-20

Set up the stop address upper 4bit which has memory access to the Card in Memory

Window 4.

8.47	Memory Window 4 Offset Low Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 34h | 834 | PPM4O | RW | MO19 | MO18 | MO17 | MO16 | MO15 | MO14 | MO13 | MO12 | 00h |

# D7-D0:	Memory Window 4 Offset Address 19-12

Set up the Offset address lower 8bit which is added to the address, which has

memory access to the Card in Memory Window 4.

8.48	Memory Window 4 Offset High Address Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 35h | 835 | PPM4O | RW | E4WP | E4RG | MO25 | MO24 | MO23 | MO22 | MO21 | MO20 | 00h |

# D7:		Write Protect

# 1b:  Disable

# 0b:  Enable

# Memory write enabled.  This bit is not affected by memory

# read.

D6:		-REG Active

1b: REG#=0  Attribute memory of the Card will be accessible.

0b: REG#=1  Common memory of the Card will be accessible.

D5-D0:	Address 20-25

Set up the Offset address upper 6bit, which has memory access to the Card in

Memory Window 0.

  - ToPIC100 Card Timing Register

Write is enabled when SlotControl Register - D_LOCK ( Config. A0H-D5 ) =0.

Write is diabled when the bit is set to 1. (WRITE PROTECT)

When ToPIC100 Function Control Register - Card Timing Enable (Card16. 3Eh-D3)= 1, this

Register settings to the access timing of Card16 are valid, and read of the Register value is

enabled. When Card Timing Enable = 0, the Register settings are invalid, and 0 is always read.

(READ ENABLE)

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Bh | 83B | PPCTM | RW | INP# | - | SCY1 | SCY0 | HCY3 | HCY2 | HCY1 | HCY0 | 00h |

# D7:		INPACK#

In case of READ ENABLE, possible to read the status of INPACK# signal of the

slot IF.

# D6:		Reserved

# R/W possible.

D5-D4:	Setup Cycle

Set up Wait number inserted to Set Up Cycle of Card Access in case of READ

ENABLE.

D5    D4    WAIT CYCLE

0      0        Non

0      1      1PCICLK

1      0      2PCICLK

1      1      3PCICLK

# D3-D0:	Hold Cycle

Set up Wait Number inserted to Hold Cycle of Card Access in case of READ

ENABLE.

Wait Cycle is not inserted when READ DIABLE.

D3  D2  D1  D0   WAITCYCLE

0    0    0    0        Non

0    0    0    1      1PCICLK

.

.

1    1    1     1     15PCICLK

8.50	Audio/Video Switching Register

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Ch | 83C | PPAVS | RW | - | - | - | - | - | - | ACNT | VCNT | 00h |

# D7-D2:	Reserved

# R/W possible.

D1:		AUDIO Control

1b : ZV - AUDIO ENABLE

0b : ZV - AUDIO DISABLE  (SPKER#, INPACK# is HI fixed.)

This bit is changed working with CONFIG. 9CH-D0.

D0:		VIDEO Control

1b : ZV - VIDEO ENABLE

0b : ZV - VIDEO DISABLE

This bit is changed working with CONFIG. 9CH-D0.

( D1 – D0 can read the status of ZV Bus when ZV Configuration Register (AEh) D1, ZV

mode select bit of Configuration Register is set to 1.

1b: ZV Bus is running.

0b: ZV Bus is no in use.

When ZV mode select bit is set to 0, the value written in ZV Control Register can be

read.

D1 – D0 bit works with ZV Control Register (9Ch) bit0 of Configuration Register

mutually, and the value of this Register will be changed when 9Ch bit0 has a change.

Audio / Video have the 9Ch bit0 in common, and both D1 and D0 will be set to 1 if the

bit is set to 1.

  - ToPIC100 Function Control Register

Write is enabled when bit5 (ID_LOCK) of Slot Control Register (Config. offset : A0h) is set to

0.

Write is disabled when the bit is set to 1.

When ID_LOCK = 1, 0 is read even if the Register has a value set in it.

When ID_LOCk = 0, the value in the Register is read.

| Offset | Offset | NAME | RW | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 3Eh | 83E | PPTFN | RW | - | PCBE | - | - | CTE | - | VSSE | CPE | 00h |

# D7:		Reserved

# R/W possible.

D6:		Power Control Buffer Enable

1b : SLOT Power Supply (P-SW) control signal OFF ( Hi-Z) RIOUT = 0 in case of

BUFFER OFF  (SUSPEND)

0b : Disable

# D5-D4:	Reserved

# R/W  possible.

D3:		Card Timing Enable

1b: Enable

Card Access Timing is determined by the set in ToPIC100 Card Timing

Register  (Card16. 3Bh).

0b: Disable

Value in Card16. 3Bh is invalid.

# D2:		Reserved

# R/W possible.

D1:		Voltage Sense Status Enable

1b : Read Additional General Control Register (Card16. 16H) - D7, D6, and the VS1,

VS2 pin status can be monitored.

0b : Only the value in the Register can be read when reading Additional General

Control Register   (16H).

# D0:		Card Power Enable

# 1b : 3V Card support Enabled

# 0b : 3V Card support Disabled

This bit changes Card Power Supply that is set in Card16 Reg.02H.

# 9     CardBus   Register

9.1	Socket Event Register

This Register is used to verify the interrupt occurred by status change.

Card service reads Socket Present State Register (CB REG 008H) and this Register to

determine the cause of interrupt.

Card service must clear the field in which the interrupt is processed after the interrupt is

completed.

This Register is cleared on the following conditions.

- Resume when CardBus Socket Registers Control Reg. - Resume Reset Enable bit

(Config.Reg.:A4h - D31)=1b

- Card removed when Config.Reg.A4H - D30 ”CardBus Card Removal Reset Enable bit”=1b

- Reset of PCI Bus.

- Assert of CRST#.

Lower 4bit (D3 – D0) is reset by writing 1b.

This Register becomes invalid when Software Card Detect is selected in Detect Method

Select bit =1b of Card Detect Control Register (Config.Reg. A3h).

| Offset |  | NAME | RW | D31 |  |  | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 000h |  | PPSKE | R | - |  |  |  | PWCY | CCD2 | CCD1 | WKUP | 00h |

# D3:		PowerCycle

Indicate D3 (Socket Present State Register (CB Reg. 008H)) will change or not.

1b: Changed

0b: Not changed

D2:	 CCD2#

Indicate D2 (Socket Present State Register (CB Reg. 008H)) will change or not.

1b: Changed

0b: Not changed

D1:		CCD1#

Indicate D1 (Socket Present State Register (CB Reg. 008H)) will change or not.

1b: Changed

0b: Not changed

D0:  	CSTSCHG/WAKEUP

Indicate D0 (Socket Present State Register (CB Reg. 008H)) will change or not.

1b: Changed

0b: Not changed

9.2		Socket Mask Register

This register provides a card service with the function for controlling Status Change

interrupt case.

It masks the interrupt to Status Change interrupt cause set in Event Register.

This Register is reset at the time of resume when Resume Reset Enable bit of CardBus Socket Registers Control Register (Config. offset:A4h) is set to 1.

Also, it is reset when the card is removed (CardBus Card Removal Reset Enable bit of CardBus Socket Registers Control Register (Config. offset:A4h) is set to 1), PCI Bus is reset, and CRST# is asserted.

| Offset |  | NAME | RW | D31 |  |  | D4 | D3 | D2 | D1 | D0 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 004h |  | PPSKM | RW | - |  |  |  | MPWC | MCD2 | MCD1 | MWKU | 00h |

# D3:		PowerCycle Mask

This bit controls Status Change Interrupt when Socket Event Register - Power Cycle (CB Reg.000H-D3) is set to 1.

0b: Enable (Default)

1b: Disable

D2-D1:  	CCD2#, CCD1# Mask

0 0b: Status Change Interrupt by Card Detect is masked. (Default)

0 1b: Canceled  (  Status Change Interrupt by Card Detect is masked.)

1 0b: Canceled  (  Status Change Interrupt by Card Detect is masked.)

1 1b: Status Change Interrupt by Card Detect is not masked.

D0:  	CSTSCHG/WAKEUP Mask

This bit controls Status Change Interrupt when Socket Event Register - CSTSCHG / WAKEUP (CB Reg.000H-D0) is set to 1.

0b: Enable

1b: Disable

9.3	Socket Present State Register

This Register is read-only indicating status of socket.

Some bits are directly set by the socket signal and the others are set according to the change of socket status.

This Register is reset at the time of resume when Resume Reset Enable bit in CardBus Socket Registers Control Register (Config. offset : A4h) is set to 1,  card removal when CardBus Card Removal Reset Enable bit in CardBus Socket Registers Control Register (Config. offset : A4h) is set to 1, or reset of PCI Bus.

| Config |  | NAME | RW | D31 | D30 | D29 | D28 | D27 |  |  | D16 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 008h |  | PPSPS | R | - | - | - | - | - |  |  |  | 3000h |
|  |  |  |  | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
|  |  |  |  | - | - | CDYV | CDXY | CD3V | CD5V | BADV | DLOS | 00h |
|  |  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
|  |  |  |  | NCAD | CINT | CARD | PC16 | PWCY | CCD2 | CCD1 | STCH | 00h |

D31:		YVsocket

# “0” fixed.

# Indicate if support for Y.YV Card is possible.

# This controller supports only 5V Card and 3.3V Card.

D30:		XVsocket

# “0” fixed.

# Indicate if support for X.XV Card is possible.

# This controller supports only 5V Card and 3.3V Card.

# D29:		3Vsocket

“1” fixed.

This controller supports 3.3V Card.

# D28:		5Vsocket

“1” fixed.

This controller supports 5V Card.

# D27-14:	Reserved

“0” fixed.

D13:		YVcard

1b: Card detected has Y.YV function.

0b: Card detected does not have Y.YV function.

D12:		XVcard

1b: Card detected has X.XV function.

0b: Card detected does not have X.XV function.

D11:		3Vcard

1b: Card detected has 3V function.

0b: Card detected does not have 3V function.

D10:		5Vcard

1b: Card detected has 5V function.

0b: Card detected does not have 5V function.

D9:		BadVCCReq

This bit is set to 1b when the voltage supplied to the socket set by Card Service

indicates beyond the limit detected by CVS<2:1>,CCD<2:1># pin.

D8:		DataLost

1b: Data disappeared

Indicate the data might have disappeared when the Card was removed.

This bit is set by the following factors.

- Transaction ended abnormal.

- Data was remained at the buffer of Socket when the Card was

removed.

This bit must be reset by Card Service when Removal Event Status Change Interrupt processing.

0b: Data normal

D7:		NotACard

1b: Card inserted is not supported by this controller.

This bit is not changed until it recognizes R2 Card or CardBus Card.

(  i.e. It is set only  when Card is inserted.)

0b: No Card inserted that this controller does not support.

D6:		Card Interrupt

1b: Interrupt signal from the Card (IREQ#, CINT#) occurred.

0b: Interrupt signal not occur.

D5:		CBcard

1b: CardBus Card is inserted.

0b: CardBus Card is not inserted.

# D4:		16card

1b: R2 Card is inserted.

0b: R2 Card is not inserted.

D3:		PowerCycle

1b: Card Power Supply stable.

0b: Card Power Supply unstable.

This bit can not be set when Card Detect Block is ON.

D2:		CCD2#

Indicate CCD2# status on IF.  This bit can not be updated when Card Detect Block

is ON.

1b: CCD2# is High. (Card not inserted.)

0b: CCD2# is Low.  (Card inserted.)

D1:		CCD1#

Indicate CCD1# status on IF.  This bit can not be updated when Card Detect Block

is ON.

1b: CCD1# is High. (Card not inserted.)

0b: CCD1# is Low.  (Card inserted.)

D0:		CSTSCHG

Indicate CSTSCHG status.  This bit can not be updated when Card Detect Block is

ON.

This bit is cleared when CRST# is asserted.

1b: CSTSCHG is High (assert)

0b: CSTSCHG is Low

9.4	Socket Force Register

This Register is for Debug, and is able to change the value in Socket Event Register and Socket Present State Register by force.  However, this Register does not exist physically.

It is able to reflect data to Socket Present State Register and Socket Event Register by writing to this Register.

| Config |  | NAME | RW | D31 |  |  |  |  |  |  | D16 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 00Ch |  | PPSKF | RW | - |  |  |  |  |  |  |  | 0000h |
|  |  |  |  | D15 | D14 | D13 | D12 | D11 | D10 | D9 | D8 | PCLR |
|  |  |  |  | - | CVST | CDYV | CDXY | CD3V | CD5V | BADV | DLOS | 00h |
|  |  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
|  |  |  |  | NCAD | CINT | CARD | PC16 | PWCY | CCD2 | CCD1 | STCH | 00h |

D14:		CVStest

When 1b is written, detect CVS<2:1>, CCD<2:1>#  status and change field of

nVcard in Socket Present State Register.

This field is used for reset the nVcard field when the field is changed by force.

D13:		YVcard

Write data is written to YVcard field in Socket Present State Register, and Power

Control Register (CB REG. 010H) is reset by writing to this bit.

Since parity voltage of the Card is changed, 1b has to be set to CVStest in Socket

Force Register, and YVcard field in Socket Present State Register has to be reset

before setting Power Control Register to make power supply for the Socket.

D12:		XVcard

Write data is written to XVcard field in Socket Present State Register, and Power

Control Register (CB REG. 010H) is reset by writing to this bit.

Since parity voltage of the Card is changed, 1b has to be set to CVStest in Socket

Force Register, and YVcard field in Socket Present State Register has to be reset

before setting Power Control Register to make power supply for the Socket.

D11:		3Vcard

Write data is written to 3Vcard field in Socket Present State Register by writing

to this bit.

Power Control Register is reset when the data written to this bit is different

from 3Vcard field.

Since parity voltage of the Card is changed, 1b has to be set to CVStest in Socket

Force Register, and

nVcard field in Socket Present State Register has to be reset before setting

Power Control Register to make power supply for the Socket.

D10:		5Vcard

Write date is written to 5Vcard in Socket Present State Register by writing to this

bit.

Power Control Register is reset when the data written to this bit is different

from 5Vcard field.

Since parity voltage of the Card is changed, 1b has to be set to CVStest in Socket

Force Register, and nVcard field in Socket Present State Register has to be reset

before setting Power Control Register to make power supply for the Socket.

D9:		BadVCCReq

Write date is written to BadVCCReq field in Socket Present State Registerby

writing to this bit.

D8:		DataLost

Write data is written to DataLost field in Socket Present State Register by writing

to this bit.

D7:		NotACard

Write data is written to NotACard field in Socket Present State Register by

writing to this bit.

If the Card is in Socket (CCD1, CCD2 assert), write is invalid.

D6:		CardBus Interrupt Enable

Set up to D6 in Socket Present State Register.

D5:		CBcard

Write data is written to CBcard field in Socket Present State Register by writing

to this bit.

If the Card is in Socket (CCD1, CCD2 assert), write is invalid.

D4:		16card

Write data is written to 16card field in Socket Present State Register by writing

to this bit.

If the Card is in Socket (CCD1, CCD2 assert), write is invalid.

D3:		PowerCycle

Power Cycle bit in Socket Event Register is set by writing 1b to this bit.

However, Power Cycle bit in Socket Present State Register has no change, and IF

power supply continues to reflect on Socket Present State Register.

D2:		CCD2#

CCD2# bit in Socket Event Register is set by writing 1b to this bit.

However, CCD2# bit in Socket Present State Register has no change, and CCD2#

pin continues to reflect on Socket Present State.

Writing 0b makes no change.

D1:		CCD1#

CCD1# bit in Socket Event Register is set by writing 1b to this bit.

However, CCD1# bit in Socket Present State Register has no change, and CCD1#

pin continues to reflect on Socket Present State.

Writing 0b makes no change.

D0:		CSTSCHG

CSTSCHG bit in Socket Event Register is set by writing 1b to this bit.

However, CSTSCHG bit in Socket Present State Register has no change, and

CSTSCHG pin continues to reflect on Socket Present State.

Writing 0b makes no change.

9.5	Power Control Register

This Register controls VPP and VCC Power Supplied to the Socket.

This Register is reset by the following conditions.

- PCIRST# is active.

- nVcard field in Socket Force Register (CB Reg.00CH) is changed by force.

- Resume when CardBus Socket Registers Control Register - Resume Reset Enable bit (Config. offset : A4H-D31)=1b

- Card is removed when CardBus Socket Registers Control Register - CardBus Card Removal Reset Enable bit(Config. offset : A4h-D30)=1b

| Offset |  | NAME | RW | D31 |  |  |  |  |  |  | D8 | PCLR |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 010h |  | PPPWC | RW | - |  |  |  |  |  |  |  | 00h |
|  |  |  |  | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0 | PCLR |
|  |  |  |  | CKRN | VCC2 | VCC1 | VCC0 | - | VPP2 | VPP1 | VPP0 | 00h |

# D7:		StopClock bit

This bit controls Enable/Disable for CLKRUN# protocol in between NOVA –

Card.

1b : Enable

0b : Disable  (Default)

D6-D4:	VCC Control bit

000b : Power off   (Default )

001b : Reserved

010b : 5.0V

011b : 3.3V

1xxb : Reserved

D2-D0:	VPP Control bit

000b : Power off  (Default)

001b : 12.0V

010b :  5.0V

0 11b :  3.3V

1 x x b : Reserved

# Text boxes

TOSHIBA CORPORATION

No. 5MD3198A0001